## Slide 1: Estimating resource availability in the power5 processor
20th May 2008
Presented by Mitesh Meswani

## Slide 2: Outline
Problem Description
FPU Availability
FXU Availability

## Slide 3: How do we know if a resource is available for another thread to use?
Ideally, we want to pair a thread with low resource usage with a high resource usage
In a perfect world we know in every cycle:
  For each functional unit
    Busy or free state of the functional unit
    Number of free entries in the issue queues
    Number of free renaming registers
  Available entries in branch history table
  Number of free TLB entries
  Number of free cache lines

## Slide 4: Continued
We have the following metrics:
  Number of cycles stalled for a unit
  Number of events of a particular type, e.g., number of floating-point events
What does Stall tell us
  Unit is not available
  If no stall, we don’t know how many entries are free
What does event count give us
  Compare the maximum computation rate for the event with observed event rate
We need to combine the above to estimate resource availability

## Slide 5: Steps to Estimate Resource Availability
Step 1:
  Identify stall counters
  Identify event counters
  For each event determine maximum supported rate
Step 2: for a given resource, set thresholds for the counters to map to high and low usage

## Slide 6: POWER5 Architecture

## Slide 7: POWER5 Instruction Flow

## Slide 8: POWER5 PMU
Six groups of events can be counted per thread
900 total events
Events are tracked by groups
Monitoring is complex: have 20 groups past dispatch, 32 outstanding loads, 16 outstanding misses, speculative execution
Upon group completion, the counters will report the last condition that stalled completion, cache misses are favored over function unit stalls

## Slide 9: FPU Availability
FPU Resources:
  Two FPUs (six cycle pipe)
  Two 12-entry issue queues
  120 renaming registers
Stall Counters:
  Cycles FPR mapper was full
  Issue queue stalls:
    Cycles FPU0 full
    Cycles FPU1 full
  Completion Stalls:
    Cycles stalled for FDIV/FSQRT
    Cycles stalled for FPU instructions

## Slide 10: FPU Event Counts for each FPU (0/1)
Instructions:
  FSQRT
  FEST
  DENORM
  FMOV_FEST
  FDIV
  FRSP_FCONV
  FMA
  STF
  FPSCR
  Groups:
    SINGLE: Single precision instructions
    1FLOP: 1FLOP instruction excludes FMA
Other events:
  STALL3: stalled in pipe3
  FIN: unit produced a result

## Slide 11: FXU Availability
FPU Resources:
  Two integer units
  Two 18-entry issue queue shared with load-store unit
  120 renaming registers
Stall Counters:
  Cycles GPR mapper was full
  Issue queue stalls:
    Cycles for FXLSO stall
    Cycles for FXLS1 stall
  Completion Stalls:
    Cycles stalled for FXU instructions
    Cycles stalled for DIV instruction
    Cycles FXU0 busy and FXU1 idle
    Cycles FXU1 busy and FXU0 idle
    Cycles FXU idle
    Cycles FXU busy

## Slide 12: FXU Event Counts for each FPU (0/1)
Instructions: None!
Other events:
  FIN (produced result)

## Slide 13: Branch Prediction Hardware Availability
Branch Prediction Hardware:
  Shared three branch history tables: Two tables for two algorithms (bimodal, path correlated), one to predict the algorithm to use
  One shared 32-entry target cache to predict branch conditional to address in count register
  One 8-entry return stack per thread to predict return address of subroutine

## Slide 14: Counters for branches
Stall Counters:
  GCT_NOSLOT_BR_MPRED (Pipe is empty due to misspredictions)
Event Counters
  FLUSH_BR_MPRED
  Branch Issued
  Unconditional branch
  Predicted conditional branch with CR prediction and/or branch target prediction
  Branch Misspredicts due to target address and/or CR prediction