## Slide 1
Computer Networking: A Top-Down Approach 9th edition Jim Kurose, Keith Ross Pearson, 2025
Chapter 7 Wireless and Mobile Networks
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2025
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
V9.0. July 2025 (completely redone from scratch, not a revision of 8.*)

## Slide 2: Wireless and mobile networks: overview
Chapter goals:
understand principles of wireless networks:
  physical layer: radio, influence on higher layers
  access network: link-layer challenges/solutions in any wireless networks
  core network: the “network” layer in a wireless network
  user/device mobility: among access networks
  application-specific wireless networks: Bluetooth, satellite, IoT
wireless networks in practice:
  WiFi
  5G (with a bit of 4G)
  Bluetooth, satellite, IoT
For a more extensive treatment of wireless and mobile networks visit: https://gaia.cs.umass.edu/wireless_and_mobile_networks

## Slide 3: Chapter 7 outline
introduction
radio: the physical layer
the wireless access network
  principles, WiFi, 5G
the wireless core network
  principles, 5G
mobility
Bluetooth, satellite, IoT wireless networks

## Slide 4: Wireless and Mobile Networks: context
more mobile-broadband-connected (cellular) devices than fixed-broadband-connected devices devices (5-1 in 2019)!
  wireless connectivity even great when WiFi users considered (80% of broadband homes use WiFi)
  60% of Internet traffic from major web sites destinated to mobile device
2007
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
1000
2000
3000
4000
5000
6000
7000
8000
Mobile broadband subscribers (M)
Fixed (wired) broadband subscribers (M)
Broadband subscribers (M)
Data source: www.statista.com (1/25)
2023

## Slide 5
Wireless applications their needs
Six application areas :
Wide-area Mobile Wireless Internet Access
Local-area Mobile Wireless Internet Access
Fixed Wireless Internet Access
Satellite Networks for Internet Access and Sensing
Cable replacement
Internet of Things (IoT)
user data rate
energy
efficiency
device density
latency
area traffic capacity
mobility
high importance
medium
low
Application needs:
mobility
user data rate
energy efficiency
device density
latency
area traffic capacity

## Slide 6: Elements of a wireless network
wired network
infrastructure

## Slide 7: Elements of a wireless network
wired network
infrastructure
wireless hosts
laptop, smartphone, IoT
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility!

## Slide 8: Elements of a wireless network
wired network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., 4G/5G cell towers, 802.11 (WiFi) access points (APs)

## Slide 9: Elements of a wireless network
wired network
infrastructure
wireless link
typically used to connect device(s) to base station, also used as backbone link
multiple access protocol coordinates link access (random access, FDMA, TDMA, CDMA, polling)
various transmission rates and distances, frequency bands
Ad hoc networks: not all wireless networks are connected into a larger network

## Slide 10: Elements of a wireless network
wired network
infrastructure
wireless device radio
wireless device has different radios for different networks
iPhone16: has ~11 different radios, many antennae
  5 different cellular radios, WiFi, Bluetooth, UWB, satellite NFC, GPS
Ad hoc networks: not all wireless networks are connected into a larger network

## Slide 11: Characteristics of selected wireless links
Indoor
Outdoor
Midrange
outdoor
Long range
outdoor
10-30m
50-200m
200m-4Km
4Km-15Km
2 Mbps
4G LTE, 5G eMBB
802.11ac
802.11n
802.11g
802.11b
3.5 Gbps
600 Mbps
54 Mbps
11 Mbps
Bluetooth
802.11ax
14 Gbps
5G
10 Gbps
802.11 af,ah
Space (100’s of Km)
LEOS

## Slide 12: Wireless networks: edge and core networks
…
Mobile device
(UE)
Base station
(eNode-B)
…
Mobile device
Base station
(gNode-B)
Mobility Management Entity (MME)
Internet
Institutional wired network
=
WLAN 1
WLAN 2
Internet
edge
core
edge
core
WiFi:
5G:

## Slide 13: Chapter 7 outline
introduction
radio: the physical layer
  radio principles
  radio channels
  antennas: MIMO
  radio spectrum
  coding and modulation
the wireless access network
the wireless core network
mobility
Bluetooth, satellite, IoT wireless networks

## Slide 14: Electromagnetics: enabling communication
receiver
(1) current at one location (transmitter) ....
(2) creates an EM field in space ....
(3) induces a current at remote location (receiver)....
transmitter
slide concept: S. Rangan (NYU)

## Slide 15: Radio basics: electromagnetic waves
l: wavelength
amplitude
Electromagnetic wave has:
wavelength (l)
frequency: speed of light / wavelength = c/l
directionality (of propagation)
time-varying amplitude
wave propagation:
slide concept: S. Rangan (NYU)

## Slide 16: Radio basics: phase
The phase of a periodic signal, represents the fraction of the period covered up until time t
often measured in angular units (0 to 360)
0
90
180
270
360
degrees
time
we can code information into signal by changing signal’s phase (keeping frequency the same!)
bit value
0
0
1
0
1
1
time
signal

## Slide 17: Radio signal characteristics
Power: antenna receive/transmit energy per unit time
linear: measured in watts (or milliwatts)
logarithmic: measured in decibels (db)
PdBm = 10 . log10
PmW
1mW
(
(
example:
PmW = 250 mW (typical max
mobile transmit power)
PdBm = 10 . log10
250mW
1mW
(
(
= 24 dBm
1.00
1.0025
.9975
frequency (GHz)
power spectral density
Power spectral density:
power present in signal as a function of frequency
carrier (center) frequency
Notes: License

## Slide 18: Radio signal characteristics
Bandwidth: width (measured in Hz) of range of frequencies use by radio signal
radio frequency usage characterized by power spectral density (psd of zero means no signal power at that frequency)
bandwidth = “band” + “width” (width of frequency band used)
2.438
2.449
2.427
power spectral density (psd)
frequency (GHz)
carrier (center) frequency
22 MHz
bandwidth
Radio signal with 22 MHz bandwidth, evenly spread between 2.427, 2.429 GHz. This 22 MHz bandwidth channel corresponds to channel 6 in WiFi network)
Radio signal “bandwidth” different from link “bandwidth” (maximum transmission rate) term used by network engineers!
two meanings/usage of “bandwidth”
Notes: License

## Slide 19: Signals and Noise
interference: other transmitters/EM radiaters in same frequency band
  hundreds of consumer devices operate in unlicensed 2.4 GHz band (aka: Industrial, Scientific, and Medical band): WiFi, Bluetooth, Zigbee, satellite TV, microwave ovens, garage-door openers, baby monitors, cordless phones, wireless mics/speakers, radio-controlled drones and toys, amateur radio, ...
thermal and electronic noise in receiver:
    natural thermal variations, imperfections in electronics
Original signal, noise, and noisy received signal
Notes: License

## Slide 20: Signal to Noise Ratio (SNR)
SNR: ratio of signal power to noise power (often measured in dB)
SNR (dB) = 10 . log10
received signal power
noise power
(
(
fundamental measure of channel “quality”
SNR of 0 implies equal signal and noise
high (or low) SNR: easy (or hard) to extract signal from signal+noise
Typical ranges for current radios:
  lower limit for cellular: -10 to -6 dB
  lower limit for WiFi: 20dB
Original signal, noise, and noisy received signal
Notes: License

## Slide 21: Channel Capacity
Shannon capacity (of a communication channel): maximum rate at which data can be transmitted, given bandwidth, SNR constraints
C = B . log2
received signal power
noise power
1+
(
(
where:
  C is capacity (bits/sec)
  B is bandwidth (in Hz)
  power measured linearly (e.g., in mW)
Observations:
  C scales linearly with B (for constant SNR)
  high SNR: C scales logarithmically: little value in increasing SNR beyond a certain point
  Shannon: classic 1948 paper
Notes: License

## Slide 22: Wireless link characteristics: path loss
  Wireless radio signal attenuates (loses power) as it propagates
f: frequency
d: distance
(aka fading) reduction in power density (attenuation) of an electromagnetic wave as it propagates from transmitter to receiver
path loss
Generalized path loss ~ (fd)n :
n=2 (free space), n=(2.7,3.5) urban, n= (3,6) in building
Notes: Wikipedia figure
Put dot on the left if I change anything.
Use pointer to show that further it goes, reduction in power density.
As a wireless signal travels over a longer distance, it spreads out and covers a larger area, but its power density (or signal strength) decreases.

## Slide 23: “Hidden terminal problem” recalling ~ (fd)2 path loss
  Signal fading with~ (d)2 path loss, causes a “hidden terminal” problem:
A
B
C
space
Signal strength
(log scale)
signal detection
threshold
hidden terminals: A and B can hear each other, B and C can hear each other, but A and C can not hear each other
complicates wireless channel sharing among A, B, C
Notes: WiGig tri-band-enabled devices, which operate in the 2.4, 5 and 60 GHz bands, deliver data transfer rates up to 7 Gbit/s (for 11ad), about as fast as an 8-band 802.11ac transmission, and more than eleven times as fast than the highest 802.11n rate, while maintaining compatibility with existing Wi-Fi devices. The 60 GHz millimeter wave signal cannot typically penetrate walls but can propagate by reflection from walls, ceilings, floors and objects using beamforming built into the WiGig system.

## Slide 24: Wireless link characteristics: hidden terminals
A
B
C
Objects cause ”hidden terminals”
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
Path loss causes “hidden terminals”
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B
A
B
C
space
Signal strength
(log scale)
signal detection
threshold

## Slide 25: Wireless link characteristics: multipath
  multipath propagation: radio signal reflects off objects ground, built environment, arriving at destination at slightly different times
line of sight
(LOS) path
reflected path
reflected path

## Slide 26: Wireless link characteristics: multipath
Tc: coherence time
Coherence time:
amount of time bit is present in channel to be received
influences maximum possible transmission rate, since coherence times can not overlap
inversely proportional to
  frequency
  receiver velocity
transmitted
pulses
received
pulse
received
LOS pulse
received
multipath
pulses
time
time
received
LOS pulse
received
multipath
pulses
  multipath propagation: radio signal reflects off objects ground, built environment, arriving at destination at slightly different times

## Slide 27: Antennas
  Antennas both transmit and receive radio waves
single antenna: old school
Gigabit LTE with 4x4 MIMO
Wi‑Fi 6 (802.11ax) with 2x2 MIMO
multiple antenna: common now in wireless networks
MIMO: Multiple input
multiple output
antenna

## Slide 28: MIMO transmission: single user
Single User MIMO: spatial diversity
multiple transmit/receive antenna to/at one user at same time
exploit multipath: use multiple antennas to increase number of paths for transmitted signal between transmitter and receiver
multipath: signals arriving at receiver not the same (e.g., some at higher quality)
antenna gain: increase SNR by combining multiple signals
12 signal paths from one sender (with two antennae) to one receiver (with two antennae)
sender
receiver

## Slide 29: MIMO: spatial diversity
  increase reliability, range by sending / receiving redundant streams of information in parallel along different spatial paths between transmit and receive antennas
improved reliability: unlikely that all paths degraded at same time
improved range: multiple antennas gather more signal at receiver
sender
receiver

## Slide 30: MIMO: spatial diversity
transmitter
H1,1(x)
x
x
H2,1(x)
y1= H1,1(x)
+ H2,1(x)
y2= H1,2(x)
+ H2,2(x)
  x: signal transmitted
  yj: signal received at antenna j
  Hi,j(x): transformation of signal x from transmitter antenna i to receiver antenna j
  estimated by receiver (perhaps with sender’s help)
receiver
Transmitter
x
x
x
Receiver
y1= H1,1(x) + H2,1(x)
H1,1()
x
H1,2()
H2,2()
H2,1()
y2= H1,2(x) + H2,2(x)
x
  Signal processing at receiver?
  don’t want to just add y1, y2
  take stronger or smaller SNR of y1, y2?
  re-align phases, coherently add?

## Slide 31: MIMO: spatial multiplexing
transmitter
H1,1(x1)
x2
x1
H2,1(x2)
y1= H1,1(x1)
+ H2,1(x2)
y2= H1,2(x1)
+ H2,2(x2)
receiver
  send two different streams of information, x1 and x2 in parallel along different spatial paths from transmitter to receiver
  spatial multiplexing differs from spatial diversity
Transmitter
x1
x2
x1
Receiver
y1= H1,1(x1) + H2,1(x2)
H1,1()
x2
H1,2()
H2,2()
H2,1()
y2= H1,2(x1) + H2,2(x2)

## Slide 32: MIMO: spatial multiplexing
transmitter
H1,1(x1)
x2
x1
H2,1(x2)
y1= H1,1(x1)
+ H2,1(x2)
y2= H1,2(x1)
+ H2,2(x2)
  Two equations in two unknowns
  but Hi,j(xi) are time-varying stochastic quantities
receiver
Transmitter
x1
x2
x1
Receiver
y1= H1,1(x1) + H2,1(x2)
H1,1()
x2
H1,2()
H2,2()
H2,1()
y2= H1,2(x1) + H2,2(x2)
y1= H1,1(x1) + H2,1(x2)
y2= H1,2(x1) + H2,2(x2)

## Slide 33: Multi-user MIMO
multiple transmit antenna send to different users at same time
  “spatial multiplexing”
exploit directional antenna: send to geographically separated users at same time via beamforming
single user MIMO
multi-user MIMO

## Slide 34: Wireless radio spectrum:
radio spectrum: national asset, owned by the nation
national government determine how spectrum is used “locally”
different spectrum use types:
licensed:
dedicated use, typically by one “owner” (e.g., cellular carrier such as AT&T, Verizon)
often allocated by spectrum auction
shared:
spectrum dynamically shared among users
“incumbent” may get preferential access, others “back off”
unlicensed:
open (free) for anyone to use, conforming to rules (e.g., power transmission levels)
2.4GHz and 5 Ghz WiFi
3.5GHz “Private 5G” (aka CBRS)
Notes: License

## Slide 35: WiFi spectrum bands
2.4 GHz
Divided into 11-14 channels, depending on country
802.11
b/g/n/ax
5 GHz range
more than 150(configurable/selectable WiFi channels) of different transmission rates
802.11
a/h/n/ac/ax
6 GHz range
most recently added
more than 250 configurable/selectable WiFi channels of different transmission rates
802.11
ax/be
other 802.11 WiFi spectrum bands, but not in widespread use
Notes: https://en.wikipedia.org/wiki/List_of_WLAN_channels

## Slide 36: 5G spectrum: three spectrum bands*
Low band frequencies: (< 1 GHz range)
covers longer distances (10’s of miles), but at lower speeds (50–250 Mbps)
* No single, well-accepted ranges for “low”, “mid” and “high”
Mid-band frequencies: 1 - 6 GHz ranges
balance distances (~5 miles ?) and transmission rates (100–900 Mbps)
1.8, 3.3 GHz to 3.8 GHz, 6 GHz bands popular
High band frequencies: 25–66 GHz range (aka mmwave)
26 GHz, 40 GHz, 50 GHz, 66 GHz bands popular
short distances (< mile), high speeds (<3 Gbps)
line of sight transmission: poor penetration of trees, buildings, ...
2G
3G
2G
3G
1-2.6 GHz
3.4 - 6 GHz
4G
4G
4G
5G
5G
5G
5G

## Slide 37: Chapter 7 outline
introduction
radio: the physical layer
  radio principles
  radio channels
  antennas: MIMO
  radio spectrum
  coding and modulation
the wireless access network
the wireless core network
mobility
Bluetooth, satellite, IoT wireless networks

## Slide 38: Physical Layer: coding and modulation
Coding
Coding
Add error detection, correction bits at physical layer
Digital Modulation
Modulation
Choose digital modulation technique that maximizes number of reliably transmitted bits/sec based on observed channel impairments
e.g., in family of Quadrature amplitude modulation (QAM)
Pulse Shaping
match transmission bandwidth to channel bandwidth using pulse shaping
RF Modulation
transmit signal as an electromagnetic wave over assigned carrier frequency
Carrier: waveform at a given frequency, fc (carrier frequency), modified (modulated) with an information-bearing signal
1010001011100110101
d: original data
We won’t cover this
(look at ECE for courses)
Notes: https://en.wikipedia.org/wiki/Carrier_wave

## Slide 39: Physical Layer: Error detection, correction coding
Coding
101000100110101
01101
EDC
EDC: error detection, correction bits
additionally transmitted bits (in addition to d)
added so receiver can detect and possibly correct errors in d bits
example: parity bits, redundancy bits
d: original data
101000100110101
noisy channel
EDC’ d’
error-free
?
Y
N
01101
EDC’
d’: received data
101001100110101
received EDC’ and received d’ bits may contain errors
errors
correctable
?
Y
N
EDC used at many layers: channel (physical), link, network, transport, application layers
Notes: https://en.wikipedia.org/wiki/Carrier_wave

## Slide 40: Physical Layer: Error detection, correction coding
Wireless physical layer may add EDC bits, into addition to:
application
transport
network
link
physical
M
Ht
Hn
M
application-layer EDC bits
Ht
M
transport-layer EDC bits
link-layer EDC bits
M
Ht
Hn
Hl
original bits
101000100110101
01101
EDC+original bits
101000100110101
adding physical-layer EDC makes sense!
detect/recover locally, rather than wait for end-end
physical layer techniques adapted to local radio error characteristics
Notes: https://en.wikipedia.org/wiki/Carrier_wave

## Slide 41: Physical Layer: EDC shuffling example
Link
physical
coding
original bits from link layer, including EDC
d1 d2 d3 d4 d5 d6 d7 d8
d1 d1’ d2 d2’ d3 d3’ d4 d4’ d5 d5’ d6 d6’ d7 d7’ d8 d8’
d1 d5’ d2 d6’ d3 d7’ d4 d8’ d5 d1’ d6 d2’ d7 d3’ d8 d4’
add EDC duplicate bits in PHY
shuffle for resistance to burst errors
modulation
modulation: from bits to symbols to waveforms
A burst of noise in this interval, causing 3 bits to be unintelligible still allows receiver to determine all original bits
A burst of noise in this interval causing 3 bits to be unintelligible , with no shuffling, would mean receiver can not determine d4
Notes: https://en.wikipedia.org/wiki/Carrier_wave

## Slide 42: Modulation
Coding
Coding
Digital Modulation
Modulation
Pulse Shaping
RF Modulation
1010001011100110101
d: original data
encoding bits (1’s, 0’s) into analog RF carrier signal by changing (“modulating”) a characteristic of the RF carrier signal: amplitude, frequency, or phase.
digital modulation
time
bit value
0
0
1
0
1
1
time
amplitude
modulation
time
frequency
modulation
time
phase
modulation
Notes: https://en.wikipedia.org/wiki/Carrier_wave

## Slide 43: Modulation schemes: ASK, PSK
time
signal
Amplitude shift keying (ASK): signal’s amplitude encodes bits
1:
0:
Binary Phase shift keying (BPSK): signal’s phase encode bits
1:
0:
PSK: 0 and 1 signals out of phase by 180o, but at same carrier frequency
time
signal
bit value
0
0
1
0
1
1
time

## Slide 44: Modulation schemes: QPSK
Why stop at just two phases?
two bits grouped to become one “symbol” (2 bits -> 4 symbols)
QPSK: Quadrature Phase Shift Keying: 4 symbols encoded using 4 phases
QPSK frequency same as BPSK, but twice the data rate!
Fun interactive QPSK tool: https://www.geogebra.org/m/enkymjtg
“00”
“01”
symbol
signal
∂
∂
“10”
“11”
∂
∂
∂
∂
∂
time
signal
“00”
0
0
“10”
1
0
“01”
0
1
“01”
0
1
“11”
1
1
“11”
1
1

## Slide 45: Constellation diagrams
graphical characterization of modulation: amplitude, phase of symbols
V
45o
135o
225o
315o
p
h
a
s
e
amplitude
point in constellation diagram depicts symbol’s phase (degrees counterclockwise from east) and amplitude (distance from origin)
QPSK constellation diagram: four symbols represented by four signal waveforms:
  four different phases
  identical amplitude
QPSK constellation diagram

## Slide 46: QAM: Quadrature Amplitude Modulation
bit encodings for 4-QAM, 16-QAM, 64-QAM (for WiFi)
generalizing QPSK
m-QAM: using m different amplitude/phase values to encode log2(m) bits
64-QAM
b0b1b2b3b4b5
b0b1b2b3
16-QAM
b0b1
4-QAM

## Slide 47: Constellation diagrams: how bit errors occur
phase/amplitude of transmitted signal
phase/amplitude of received signals
16-QAM
b0b1b2b3
receiver measures amplitude, phase of received signal
receiver classifies symbol as bit pattern with amplitude, phase closest to received signal amplitude, phase
Transmitter transmits waveforms for 12 1111 symbols, sequentially
This received signal, is misclassified as 1011 since its amplitude, phases are closer to 1011 than 1111
These received signals correctly classified as 1111 (received amplitude, phases closest to 1111)

## Slide 48: Adaptive modulation
given modulation scheme :
has nominal data rate (assuming no errors)
SNR can increase/decrease:
  changing interference
  sender transmitter power
  move along SNR vs BER tradeoff curve
Idea: change modulation scheme, power on the fly, getting highest data rate possible (at acceptable BER, acceptable energy expenditure), as SNR changes
Max data rate:
16 QAM: 11.5 Mbps
64 QAM: 26.9 Mbps
Notes: Direct Relationship: As SNR increases, BER generally decreases. A higher SNR means that the signal is more distinct from the noise, making it easier for the receiver to correctly interpret the transmitted bits.
Design Considerations: Achieving a high SNR often requires more power or more advanced technology (like better antennas or receivers), which can be more expensive or consume more energy.

## Slide 49: Chapter 7 outline
introduction
radio: the physical layer
the wireless access network
  sharing a wireless access channel: OFDMA, CSMA/CA
  WiFi wireless LAN
  5G radio access network
the wireless core network
  principles, 5G
mobility
Bluetooth, satellite, IoT wireless networks

## Slide 50: Recall: MAC protocols
multiple access protocols
channel partitioning
random access
taking turns
type of MAC
OFDMA
CSMA/CA
TDMA
FDMA
Aloha
slotted Aloha
CSMA
CSMA/CD
(Ethernet)
polling
type of protocol
system
OFDMA: 4/5G, WiFi6; Bluetooth; satellite
  WiFi; satellite; control plane: 4/5G, Bluetooth
  (and many wired technologies)
  Bluetooth, satellite
  (and many wired technologies)
Notes: Control plane: coordination about how to share the data plane requires used of the channel.

## Slide 51: FDM: Frequency Division Multiplexing
0.00
0.25
0.50
- 0.25
- 0.50
frequency (Hz)
rather than one fat “wideband” channel:
divide into multiple thin “narrowband” subchannels
separated by “guard bands” to avoid interference
Narrowband channels:
each subchannel has lower bit transmission rate than wideband channel:
  making multipath easier to accommodate
  lower rate implementations easier
transmissions can happen on different subchannels at same time (in parallel)
Notes: Within each Wi-Fi channel, OFDM splits the channel's bandwidth into many subcarriers.

## Slide 52: OFDM: Orthogonal FDM
∂
∂
subcarriers: again close together
slightly overlapping, but no guard bands
0.00
0.25
0.50
- 0.25
- 0.50
frequency (Hz)
orthogonal: carefully designed, modulated so crosstalk among subcarriers cancels at center of each subcarrier frequency
envelope of spectrum

## Slide 53: OFDM: Subcarriers
∂
0.00
0.25
0.50
- 0.25
- 0.50
frequency (Hz)
# subcarriers in an 4G / 5G channel depends on channel’s bandwidth
Channel bandwidth (MHz)
Number of subcarriers
1.25
2.5
5
10
15
20
76
150
300
600
900
1200
Wireless Jargon:
“carrier” ~ “channel”
“subcarrier” ~ “subchannel”
Notes: This example shows 12 subcarriers, in “real life”

## Slide 54: OFDMA: subcarriers, time
Time
15 kHz
180 kHz
frequency

## Slide 55
frequency
time
66.6 umsec
0.5 msec slot
one “symbol” can be transmitted per 66.6 usec (4G) at given subcarrier frequency
number of bits (between 2-8) in symbol depends on modulation technique chosen (which depends on channel quality)
OFDMA: symbols

## Slide 56: OFDMA: resource blocks
frequency
time
66.6 umsec
0.5 msec slot
resource block (RB):
symbols grouped into resource blocks
84 symbols (7 symbols/slot over 12 subcarriers) in 4G
smallest unit of data that can be sent to (assigned to) a user

## Slide 57: OFDMA: resource blocks
Base station decides which RBs get assigned (over all frequencies) to which devices at 1 msec intervals
1 msec
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
frequencies
4G / 5G scheduling interval

## Slide 58: From 4G LTE to 5G New Radio (NR)
Commonalities, differences:
4G, 5G both use OFDMA
Subcarrier bandwidths:
  4G: 15 kHz
  5G: 15, 30, 60, 120 kHz
Max carrier bandwidth:
  4G: 20 MHz
  5G: 100 MHz
4G, 5G: resource blocks (RB)
smallest scheduling unit of transmission to device
14 symbols/subcarrier
1 msec
1 5G NR PRB
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
7 symbols/subcarrier
0.5 msec
1 LTE PRB
12 (or configurable) number of subcarriers per carrier
4G
5G
configurable bandwidth
per sub carrier

## Slide 59: CSMA/CA: addressing the “hidden terminals” problem
A
B
C
Objects cause ”hidden terminals”
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
Path loss causes “hidden terminals”
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B
A
B
C
space
Signal strength
(log scale)
signal detection
threshold

## Slide 60: CSMA/CA: collisions happen
DIFS
data
data
A senses channel empty, transmits
DIFS
B senses channel empty (A’s’ transmission has not reached B yet), transmits
collision
data
A senses channel empty, transmits
DIFS
B senses channel empty (does not hear A’s transmission due to fading), transmits
collision
data
A
B

## Slide 61: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no collision detection)
sender
receiver
DIFS
data
SIFS
ACK
802.11 receiver
if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  3. if no ACK, increase random backoff interval, repeat 2 (see next slide)

## Slide 62: CSMA/CA: randomization after collision
DIFS
data
data
A senses channel empty, transmits
DIFS
Channel sensed idle for DIFS time
collision
A
B
data
data
Transmit (successfully)
NO ACK, loss or collision detected
No ACK: loss or collision detected
DIFS
Wait DIFS time
DIFS
Wait DIFS time
Wait randomized backoff
Wait randomized backoff [0, ~200 msec], depending on PHY. Backoff interval doubles after each collision
random
backoff
random
backoff

## Slide 63: Avoiding collisions: using RTS/CTS
idea: sender “reserves” channel use for data frames using small reservation packets
sender first transmits small request-to-send (RTS) packet to BS using CSMA
  RTSs may still collide with each other (but they’re short)
  contains duration for following data transmission
BS broadcasts clear-to-send (CTS) packet in response to RTS
  contains duration for following data transmission
RTS and/or CTS heard by all nodes
  All nodes except transmitter defer transmissions
  transmits data frame
Notes: Ready to send and clear to send

## Slide 64: Collision Avoidance: RTS-CTS exchange
AP
A
B
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer
time

## Slide 65: Backwards compatibility: challenging
IEEE standard | WiFi gen | Year | Max data rate (theoretical) | Frequency (GHz) | Bandwidth | PHY
802.11b |  | 1999 | 11 Mbps | 2.4 | 22 | spread spectrum
802.11g |  | 2003 | 54 Mbps | 2.4 | 20 | OFDM
802.11n | WiFi 4 | 2009 | 600 Mbps | 2.4, 5 | 20, 40 | OFDM
802.11ac | WiFi 5 | 2013 | 6.9 Gbps | 5 | 20, 40, 80,160 | OFDM, MIMO
802.11ax | WiFi 6 | 2020 | 9.5 Gbps | 2.4, 5 | 20, 40, 80,160 | OFDM, OFDMA, MIMO
802.11be | WiFi 7 | 2024 | 30+ Gbps | 2.4, 5, 6 | 20, 40, 80,160, 320 | OFDM, OFDMA, MIMO
Challenge: WiFi 6/7 APs support OFDM (FDMA) and OFDMA (FDMA+TDMA)
How can a WiFi 6/7 AP do both FDMA and TDMA at the same time?
How can WiFi 6/7 AP support user device radios that only do FDMA?

## Slide 66: Extending RTS/CTS: Multiuser RTS
idea: create new type of RTS message Multiuser RTS (MU-RTS)
transmitter must use MU-RTS before OFDMA transmissions
transmit MU-RTS using full FDMA channel, with duration info (as usual )
  heard by all 802.11* devices (both OFDM- and OFDMA-capable)
  contains additional OFDMA assignment info for receivers (so receivers will know which OFDMA RUs to listen to)
receivers respond with CTS, sent on assigned OFDMA subchannel
transmitter sends resource blocks to OFDMA receivers, according to assignment
Notes: Ready to send and clear to send

## Slide 67: Extending RTS/CTS: Multiuser RTS
Example scenario:
AP wants to send to seven devices
two legacy devices a, b (OFDM only)
five OFDMA-capable devices 1, ... 5
RTS
(business-as-usual for devices a,b)
MU-RTS
(for OFDMA devices 1 ... 5)
Notes: Ready to send and clear to send

## Slide 68: Chapter 7 outline
introduction
radio: the physical layer
the wireless access network
  sharing a wireless access channel: OFDMA, CSMA/CA
  WiFi wireless LAN
  5G radio access network
the wireless core network
  principles, 5G
mobility
Bluetooth, satellite, IoT wireless networks

## Slide 69: 802.11 wireless link layer
data plane
WLAN
Link layer
Application
Network
Physical
Transport
802.11 MAC
control plane
802.3 MAC
PHY
802.11 MAC
PHY
data plane
control plane
802.3 MAC
PHY
802.11
802.3

## Slide 70: 802.11 downlink (AP-to-device) frame flow
AP
UEs
to/from institutional
network, Internet
reliable
data transfer
energy
management
channel
measurement
discovery,
attachment
RTS/CTS
...
control plane
data plane
PHY
control frame
mngmnt frame
mngmnt frame
control frame
...
...
IP datagram
IP datagram
IP datagram
...
data frame
data frame
data frame
queue of frames awaiting transmission
(MAC scheduling)
data frames: containing IP datagrams
Control, management frames

## Slide 71: 802.11 frame: addressing
2
2
6
6
6
2
6
0 - 2312
4
Address 1: MAC address of wireless host or AP to receive this frame
Address 4: used only in ad hoc mode
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 3: MAC address of router interface to which AP is attached

## Slide 72: 802.11 frame: addressing
Internet
H1
R1
AP MAC addr
address 1
address 2
address 3
802.11 WiFi frame
R1 MAC addr
H1 MAC addr
R1 MAC addr
MAC dest addr
MAC source addr
802.3 Ethernet frame
H2 MAC addr

## Slide 73: 802.11 frame
2
2
6
6
6
2
6
0 - 2312
4
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
seq
control
duration of reserved
transmission time (RTS/CTS)
frame sequence # (for reliable data transfer)
2
2
4
1
1
1
1
1
1
1
1
type
from
AP
subtype
to
AP
more
frag
WEP
more
data
power
mgt
retry
rsvd
protocol
version
0: management
1: control
2: data
IP datagram, link-layer control or management message
type of management, control, or data frame
Notes: https://howiwifi.com/2020/07/13/802-11-frame-types-and-formats/

## Slide 74: Retrospective: “A day in the life”* (WiFi)
Application
Network
Physical
Transport
802.11 MAC
control plane
802.11 MAC
Physical
data plane
control plane
data plane
*https://gaia.cs.umass.edu/kurose_ross/videos/6/
HTTP
1
1
HTTP/3 request in UDP segment, in IP datagram, into 802.11 frame. Enter, wait, MAC frame scheduling queue
RTS
CTS
2
Device sends RTS control frame (using CSMA/CA); AP responds with CTS.
3
Device sends DATA frame to AP. Buffers DATA frame
2
3
ACK
4
AP responds with ACK, device removes transmitted frame
4
AP can now forward frame to router

## Slide 75: Chapter 7 outline
introduction
radio: the physical layer
the wireless access network
  sharing a wireless access channel: OFDMA, CSMA/CA
  WiFi wireless LAN
  5G radio access network (RAN)
the wireless core network
  principles, 5G
mobility
Bluetooth, satellite, IoT wireless networks

## Slide 76
Architectural Elements of 5G
radio access
Network (RAN)
to
Internet
5G core network
gNodeB
User device
Core Network Functions

## Slide 77
5G Radio Access Network (RAN)
gNodeB
User equipment
(UEs)
5G RAN: edge network connecting devices to base station
provides link-layer service, as first hop between devices and larger network
limited geographic scope
under control of a single service provider
somewhat analogous to WiFi LAN
RAN components:
  many devices (User Equipment: UE)
  radio channel (New Radio: NR)
  one base station (Next Generation Node B: gNodeB, gNB)

## Slide 78
5G Core Network
to
Internet
Core Network Functions
Core situated between RAN and other endpoints (Core, larger Internet)
  single Core; multiple RANs
consist of links, routers, servers, providing services to devices and base stations
  “all IP” Core, but very different services than traditional Internet apps
clear logical separation between control-plane, user plane:
  CUPS: Control-Plane and User-Plane Separation

## Slide 79: Resource Blocks (RB)
  Resource Element (RE): holds one transmitted OFDMA symbol, in one time minislot on one subcarrier frequency
  Resource Block (RB): bundle of neighboring (time, frequency) Resource Elements
    4G: 84 symbols (12 neighboring subcarriers, 7 consecutive minislots)
    5G: multiple bundlings possible
    RB is smallest unit of transmission scheduling: all symbols in RB have same source, destination
180
kHz
1 ms
10 MHz channel with 50 RBs.
each RB spanning 180 kHz subchannel
time
4G Resource Block (RB): 84 Resource Elements (REs), each carrying one symbol.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.

## Slide 80: 5G Bands, Channels, Subchannels: it confusing!
  ... and it’s about to get more confusing
180
kHz
1 ms
10 MHz channel with 50 RBs.
each RB spanning 180 kHz subchannel
time
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
channel N
channel 1
one band
multiple channels
multiple subchannels
per channel
...
...
...
...

## Slide 81: Downlink physical channels
downlink RBs transmitted from base station to devices
three 5G downlink physical channels:
  Physical Downlink Shared Channel (PDSCH)
  Physical Downlink Control Channel (PDCCH)
  Physical Broadcast Channel (PBCH)
base station
set of Resource Blocks (RBs) carrying similar type of data (channel information RBs, user and control RBs, RB allocation information)
Physical channel
...

## Slide 82: Uplink physical channels
uplink RBs transmitted from devices to base station
three 5G uplink physical channels:
  Physical Uplink Shared Channel (PUSCH)
  Physical Random-Access Channel (PRACH)
  Physical Uplink Control Channel (PUCCH)
set of Resource Blocks (RBs) carrying similar type of data (radio channel information RBs, user and control RBs, RB allocation information)
Physical channel
...
base station

## Slide 83: Uplink/downlink logical channels
Set of Resource Blocks (RBs) carrying similar type of data. Logical channels are mapped onto physical channels, with one or more logical channel mapped to same physical channel
individual, per-device logical channels, as well as shared logical channels among devices
logical channel
6 physical channels
many logical channels
...
...
base station

## Slide 84
RAN
link
layer
PDCP
RLC
MAC
Physical
RRC
SDAP
control
plane
Network
user plane
device
base station
PDCP
RLC
MAC
Physical
RRC
RAN
link
layer
SDAP
control
plane
Network
user plane
Transport
Application
RAN protocol stack (at device, base station)

## Slide 85
PDCP
RLC
MAC
Physical
RRC
SDAP
control
plane
Network
user plane
device
base station
PDCP
RLC
MAC
Physical
RRC
SDAP
control
plane
Network
user plane
Transport
Application
HTTP
1
SR
DCI
Retrospective: “A day in the life”* (5G RAN)
1
HTTP/3 request in UDP segment, in IP datagram, into 5G frame. Enter, wait, 5G MAC frame scheduling queue
2
device’s control plane sends SR Scheduling Req) on Physical Uplink Control Channel (PUCCH) to base station
3
base station control plane send DCI message Physical Downlink Control Channel (PDCCH) granting upstream RBs
4
device sends frame in allocated RBs
2
3

## Slide 86: RAN packet processing pipeline: context
Base station
(gNode-B)
RAN: transfers datagrams between mobile core and devices
IP datagrams
device
datagrams
protocol processing pipeline in UE

## Slide 87: RAN packet processing pipeline
RRC
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
base station
control
plane
user
plane
mobile
core
traditional 3GPP view
datagrams
RRC (Radio Resource Control)
configures coarse-grained, policy-related aspects of pipeline (e.g., scheduling prioritization, security)
this implements the RAN’s control plane
does not process user plane packets

## Slide 88: RAN packet processing pipeline
RRC
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
base station
control
plane
user
plane
mobile
core
PDCP (Packet Data Convergence Protocol)
compress/decompress IP headers
ciphering, integrity protection
datagrams

## Slide 89: RAN packet processing pipeline
RRC
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
base station
control
plane
user
plane
mobile
core
RLC (radio link control)
link-layer frame segmentation/reassembly
reliable data transfer (ARQ)
datagrams

## Slide 90: RAN packet processing pipeline
RRC
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
base station
control
plane
user
plane
mobile
core
MAC (Media Access Control)
buffering, multiplexing/demultiplexing frames
scheduling: real-time scheduling frame decisions
I msec scheduling control loop
datagrams

## Slide 91: RAN packet processing pipeline
RRC
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
base station
control
plane
user
plane
mobile
core
PHY (Physical Layer)
modulation, coding
datagrams

## Slide 92: Split RAN
  Q: how is RAN functionality partitioned between physical elements (i.e.,., “split” across centralized and distributed locations)?
    historically: no split - implemented in base station
RRC
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
Monolithic base station
control
plane
user
plane
datagrams

## Slide 93: Split RAN
  Q: how is RAN functionality partitioned between physical elements (i.e,., “split” across centralized and distributed locations)?
    historically: no split - implemented in base station
RRC
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
Central Unit (CU)
control
plane
user
plane
Distributed Unit (DU)
Radio Unit (RU)
    O-RAN: three “units” - where units are implemented is an implementation choice
datagrams

## Slide 94: Software-defined RAN
Recall our earlier description of traditional RAN base station (below)
tightly coupled control and data planes
let’s focus on control / management: RRC implementation

## Slide 95: Software-defined RAN
  SD-RAN: implementing RAN using SDN approach
Control plane proxy
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
control
plane
user
plane
Real-Time Intelligent Controller (RIC)
3GPP-compliant interface between RAN and Mobile Core control plane
New programmatic API for exerting software-based control over pipeline that implements RAN user plane
Re-factored RRC
SDN-controlled switches

## Slide 96: Software-defined RAN
  SD-RAN: implementing RAN using SDN approach
Control plane proxy
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
control
plane
user
plane
Real-Time Intelligent Controller (RIC)
Re-factored RRC
SDN-controlled switches
RAN Network Information Base (R-NIB)
common set of information consumed by numerous control apps, e.g., longer time-scale CQI (channel Quality Indicator) values, other per-session state
R-NIB
load
balancing
handover
QoS
Near-real time network control applications implemented as “xApps”
…
…

## Slide 97: RAN: operator’s “secret sauce”
    combination of standardized specifications + implementation strategies:
      interfaces, high-level functions standardized
      implementation of some functions, e.g., RB assignment to channels, frame scheduling, not standardized – up to the network operator.
      implementation choices are the technical “secret sauces”

## Slide 98: Chapter 7 outline
introduction
radio: the physical layer
the wireless access network
  sharing a wireless access channel
  WiFi wireless LAN
  5G radio access network
  common challenges: network discovery, frame scheduling, energy
the wireless core network
  principles, 5G
mobility
Bluetooth, satellite, IoT wireless networks

## Slide 99: Joining the edge wireless network
arriving device: must establish initial connection with node (WiFi AP, 4G/5G base station) at wireless edge of network
  initial connection then used for authentication, DHCP, gain full network access
  “bootstrapping” connectivity: initial connection is just with edge node
institution’s
wired network
Internet
gNode-B
Mobile packet core
Internet
WiFi AP
WiFi
5G
association

## Slide 100: Association: two approaches
Beaconing: mobile listens to wireless channels for “beacons” advertising existence of wireless network node(s)
Probing: mobile actively transmits probe messages, waits for wireless network node(s) to reply
user device
Edge network 1
Edge network 2
base
station
base
station
probe request
reply
reply
user device
Edge network 1
Edge network 2
base
station
base
station
beacon
beacon
Either (or both) approaches used in practice in an edge network

## Slide 101: 802.11: beaconing and probing
arriving client device
WiFi AP
1
802.11 beacon frame (broadcast)
2
802.11 Association request
3
802.11 Association response
Beaconing:
... device will next authenticate to network
AP 2
AP 1
H1
2
2
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1
Probing:
1
1
2
2
3
4
2
3
4
No exchange of identity, credentials (yet)! Just “Can we talk?”

## Slide 102
Connecting to the 5G edge
5G network
(network 1)
5G network
(network 2)
H1
Base station 1
1
network 1’s SSB, SIBs
1
network 2’s SSB, SIBs
3
2
RRC connection setup request
RRC connection setup response
Base station 2

## Slide 103: RAN/WLAN scheduling: the “big picture”
All packets to/from all devices in edge network must pass through base station
4G/5G and WiFi 6/7: OFDMA RB scheduling
downlink MAC scheduler: which frames to send from base station to which devices in which order in which RBs (if OFDMA)?
uplink MAC scheduler: which devices send which frames in which order in which RBs to base station (if OFDMA)
gNodeB
devices
5G RAN
AP
devices
Wi-Fi
PHY
MAC
PHY
MAC

## Slide 104: Wireless MAC scheduling: considerations
Channel aware or channel unaware?
does scheduler consider quality of channel between base station and device?
good
poor
QoS aware or QoS unaware?
does scheduler consider QoS (quality of service) needed by (or guaranteed to) device?
voice
WWW browsing
Priorities, Fair scheduling?
Does scheduler provide priority among different types of traffic (user, control, real-time)?
does scheduler consider fairness among UEs?
fairness: no standard definition
“We are all equally important”

## Slide 105: MAC scheduling considerations
Channel aware or channel unaware?
does scheduler consider quality of channel between base station and device?
good
poor
QoS aware or QoS unaware?
does scheduler consider QoS (quality of service) needed by (or guaranteed to) device?
voice
WWW browsing
Priorities, Fair scheduling?
Does scheduler provide priority among different types of traffic (user, control, real-time)?
does scheduler consider fairness among UEs?
fairness: no standard definition
“We are all equally important”
Standards do not dictate answers to these questions!
Scheduling algorithms, parameters up to network implementers, operators: their “secret sauce”

## Slide 106: RAN scheduling: Resource Blocks
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
A 10 MHz channel with
50 RBs, each RB spanning 180 kHz
180
kHz
Scheduling:
Base station decides which frames/packets get assigned to which RBs for transmission to user
scheduling interval: 1 msec
scheduling complexity:
  50 subchannels per 10MHz channel
  100’s (?) active user
Resource Block: 84 symbols
one user gets to transmit 84 symbols on one subchannel in 0.5 sec time interval
50 subchannels per 10MHz channel
1 ms
time

## Slide 107: RAN scheduling: Channel Quality Indicator
PDCP
RLC
MAC
PHY
RAN packet-processing stack (3GPP)
IP datagrams
Channel Quality Indicator (CQI):
user measures quality of received reference signals (embedded in RBs), reports quality back to base station
4-bit CQI value maps to modulation scheme to use (e.g., which QAM?) and expected throughput
scheduler
“We are all equally important”
control plane (RRC)
CQI

## Slide 108: RAN scheduling: QoS Class Indicator
PDCP
RLC
MAC
PHY
RAN packet-processing stack (3GPP)
IP datagrams
QCI: QoS Class Indicator
QoS network wants to provide to a particular device (e.g., delay, guaranteed bit rate QoS guarantees)
scheduler determines allocation of available radio spectrum to ensure all UEs meet their QoS requirements
scheduler
Priority | QCI | Max delay | Max loss | Application
2 | 1 | 100ms | .01 | Voice
3 | 4 | 50 ms | .001 | Real-time gaming
6 | 7 | 300 ms | .000001 | Streaming video
8 | 8 | 600 | .000001 | Web browsing, TCP
CQI
QCI
(RRC)

## Slide 109: 4G/5G scheduling: abstraction

## Slide 110: Scheduling policies: priority
Priority scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification, e.g., control versus user data
high priority queue
low priority queue
arrivals
classify
departures
link
1
3
2
4
5
arrivals
departures
packet in service
send packet from highest priority queue that has buffered packets
  scheduling within priority class could be another scheduling discipline
1
3
4
2
5
1
3
2
4
5

## Slide 111
Each device has its own queue
scheduler cyclically scans device queues, mapping packets/frame from each device (if available) to an RB in turn
channel unaware, QoS unaware
fair (by turns) but not necessarily throughput-fair since different devices may have different channel quality
Round Robin scheduling (per UE)

## Slide 112
find device (UE) i, with highest quality channel over all RBs, k:
    dik(t): expected data rate for UEi using kth RB at time t (e.g., based on CQI)
    at t: select maxi,k {dik(t)}, assign UEi frame to RBk
maximizes overall immediate throughput
channel aware, QoS unaware, throughput unfair
Maximum Throughput (MT) scheduling

## Slide 113
Blind Equal Throughput (BET) scheduling (per device)
scheduler maintains exponentially-weighted-moving-average of data rate received at each UEi at time t, Ri(t):
Ri(t) = (1-b) . ri(t) + b . Ri(t-1)
  where ri(t) is data rate achieved in scheduling interval t
at t: select mini {Ri(t-1)}: assign UEi frame blindly (not know channel conditions) to (any) RB
  assign RB to device with smallest data rate last round
channel somewhat-aware, QoS unaware, blind throughput fair

## Slide 114
combine Blind Equal Throughput (BET) and Maximum Throughput (MT) scheduling
    dik(t): expected data rate for UEi using kth RB at time t
    Ri(t-1): data rate achieved by UEi at t
at t: select maxi,k {dik(t) / Ri(t-1)}: assign UEi
Proportional Fairness (PF) scheduling
balances high data rate with a measure of fairness
channel aware, QoS unaware, fairness aware

## Slide 115: Energy consumption in wireless devices
battery/energy: a critical resource in wireless devices (phones, IoT)
energy use by LTE radios1:
  on: transmitting or receiving/waiting to receive: 1000 — 3500mW
  off: < 15mW (~1% – 2 % of on-state energy use)
significant amount of device energy expended on communication, across applications
5G implementations currently expending more energy than 4G
Power use in mobile phones: app vs screen vs system vs network
Sources: 1: ATT, 2: “Understanding Operational 5G,” ACM SIGCOMM 2020

## Slide 116: Cycles of sleep/activity: sleep
4G/5G, WiFi, Bluetooth radios turned off when not in use: conserve energy
Going to sleep is easier:
device-driven: go to sleep if nothing to send, nothing being received
sleep may (or may not) be coordinated with base station (4/5G), AP (WiFi) , controller (BT)
may have deep-sleep (longer, more “turned off”) versus light sleep (shorter, less “turned off”)

## Slide 117: Cycles of sleep/activity: awake
4G/5G, WiFi, Bluetooth radios turned off when not in use: conserve energy
Waking up is harder:
base station (4/5G), AP (WiFi) , controller (BT) needs to signal to “wake up” device when there are packets to be sent to it
  network context (4/5G) may need to be re-created
  data frames containing IP datagram (e.g., from remote hosts) need to be buffered at base station until device is awake

## Slide 118: Cycles of sleep/activity: tradeoff/challenges
How long to sleep?
longer: save more energy but greater latency
  effects on high-layer protocols: e.g., TCP
shorter: less energy savings, and more signaling overhead with short sleep cycles
How long to stay awake?
time since last activity (before going to sleep)
  data transmission typically “bursty”
  burst should be over before going to sleep: how long to wait?

## Slide 119: Coordinated wake/sleep in 5G
transmission received at device, start inactivity timer
incoming transmission to device buffered at base station until end of current DRX cycle
Device awakes from long DRX sleep, accepts channel scheduling assignment, ends sleep
device active
inactivity timer timeout, enter short DRX cycle
device active
periodic wakeup in short DRX cycles, nothing to send/receive, return to short DRX sleep
short DRX cycles
still nothing to send or receive, enter long DRX cycle
long DRX cycles
time
t0
t1
t2
t4
t3
transmission received at device
t5

## Slide 120: Chapter 7 outline
introduction
radio: the physical layer
the wireless access network
  principles, WiFi, 5G
the wireless core network
  principles, 5G
mobility
Bluetooth, satellite, IoT wireless networks

## Slide 121: 5G Core Functional Components
user plane
control plane
base station
AMF
Access, Mobility
Management
AUSF
Authentication
Server
SMF
Session
Management
UPF
User
Plane
NEF
Network Exposure
AF
Application Function
NRF
Network Repository
PCF
Policy control
UDM
Unified Data Management
UDSF
Unstructured Data Storage
UDR
Unified Data Repository
SEPP
Security Edge Proxy
data
storage
control planes in other cellular providers
3rd party apps
Internet
N1
N2
N3
5G Core is all (mostly) about control plane services

## Slide 122: 5G Core Functional Components
UPF (User Plane Function)
each device is assigned to a UPF, which acts as relay, forwarding traffic between UE, Internet
UPF responsible for policy enforcement, lawful intercept, traffic usage measurement, QoS policing
responsible for tunneling (i.e., encapsulating, decapsulating) traffic to/from base station over N3 interface

## Slide 123: 5G Core Functional Components
AMF (Access, Mobility Management Function)
connection, reachability management; mobility management; access authorization; and location services
SMF (Session Management Function)
manages each UE session, including IP address allocation, selection of associated UP function, QoS control, control aspects of UP routing

## Slide 124: 5G Core Functional Components
AUSF (Authentication Server Function): Authenticates devices.
UDM (Unified Data Management): Manages user identity, including the generation of authentication credentials.
UDR (Unified Data Repository): Manages user static subscriber-related information.
UDSF (Unstructured Data Storage Network Function): Used to store unstructured data, and so is similar to a Key/Value Store.

## Slide 125: 5G interfaces*, control/user -plane separation (CUPS)
control plane
emphasis on functions and services
well-defined interfaces defines between services
base station
N2
N7
N5
N13
N12
N10
N8
N4
N3
N1
N11
base station
S-GW
data plane
5-layer Internet data plane
extensive use of tunneling
IP tunnel
N3
N6
N6
AMF
Access, Mobility
Management
SMF
Session
Management
PCF
Policy control
AUSF
Authentication
Server
UDM
Unified Data Management
AF
Application Function
UPF
User
Plane
IP datagrams
* not all 3GPP defined interface shown

## Slide 126: 5G Core: User plane tunnels
from Internet,
sender has IP address w
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
GTP-U
UDP
IP
link
Physical
GTP-U
UDP
IP
link
Physical
IP
link
Physical
UPF for device z
UPF address: x
Source
addr: w
user payload
Dest
addr: z
Source
addr: w
user payload
Dest
addr: z
Source
addr: x
Dest
addr: y
Source
addr: w
UE payload
Dest
addr: z
base station
address y
backhaul network
user device,
address z

## Slide 127: Identity: who are you?
  Internet approaches:
  You’re a name, password
    different names, password for different applications, services
  You’re a name, public key certificate
    servers often have public keys, users not so much (yet)
  4G/5G:
  You’re a customer to a wireless service provider, with a home cellular network (who you pay)
  you have a SIM (Subscriber Identity Module) card or vSIM
    identifies you, your home network to all cellular networks globally
    has cryptographic key info also known to your home network
Notes: Section 4.6.1 (pg 247) in Sauter 4th edition

## Slide 128: Joining a 5G network
Two major phases:
  Registration: device identifies, authenticates itself to network, and vice versa
  PDU Session establishment: Core network functions allocate IP address to device, create data-plane path between device and device’s UPF
    PDU: protocol data unit, aka, “packet”
Access and Mobility Management Function (AMF) plays key role in joining arriving device into network

## Slide 129: Joining a 5G network: steps
AMF
Access, Mobility
Management
UDM
Unified Data Management
RRC connection setup
request, response
Identity request, response
Registration request
AUSF
Authentication
Server
remote/home
5G Core
registration accept
SMF
Session
Management
PDU session establishment request
registration
session creation request, response
device subscription retrieval, update
UPF
User Plane Function
session
establishment req./resp.
session info (e.g., device IPv4 address, tunnel)
session req. (with SMF info)
session response
Device, base station, RAN data plane configuration
1st uplink datagram in data plane
session
establishment
authentication, security
authentication, security
update device’s connection data
AUSF
Authentication
Server

## Slide 130: Chapter 7 outline
introduction
radio: the physical layer
the wireless access network
  principles, WiFi, 5G
the wireless core network
  principles, 5G
mobility
Bluetooth, satellite, IoT wireless networks

## Slide 131: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
device moves
between networks, but
powers down
while moving
device moves within same WLAN/RAN in
one provider
network
device moves
among multiple
provider networks,
while maintaining
ongoing connections
device moves among WLANs/ RANs in
one provider
network
We’re interested in these!

## Slide 132: Mobility in a WiFi network
AP1
BSS1
AP2
AP3
BSS3
BSS2
Extended Service Set (ESS)
router R1
switch S2
Internet
switch S1
802.11: a link-layer standard, takes a link-layer approach towards mobility
Extended Service Set (ESS): multiple BSS’s, in same layer-3 subnet, each with same SSID
mobility between BSSs in same ESS
  Fast re-authentication
  AP can suggest new APs to device
proprietary (vendor) solutions for enhanced mobility

## Slide 133: Mobility in 5G networks: handover
Handover:
mobile device changes is point of attachment to the network
data flow to device changes from source base station to target base station
AMF
Access, Mobility
Management
SMF
Session
Management
UPF
User Plane Function
before
handover
after
handover
Why perform handover?
stronger signal from target base station
target base station has less devices, less traffic

## Slide 134
source BS
1
3
2
data path before handover
data path after
handover
1
current (source) BS selects target BS, sends Handover Request message to target BS
2
target BS pre-allocates radio time slots, responds with HR ACK with info for mobile
3
source BS informs mobile of new BS
mobile can now send via new BS - handover looks complete to mobile
4
source BS stops sending datagrams to mobile, instead forwards to new BS (who forwards to mobile over radio channel)
target BS
4
UPF
User Plane Function
Mobility in 5G networks: handover

## Slide 135
UPF
User Plane Function
source BS
target BS
5
5
target BS informs AMF, SMF that it is new BS for mobile
SMF instructs UPF to change tunnel endpoint to be (new) target BS
AMF
Access, Mobility
Management
SMF
Session
Management
6
UPF
User Plane Function
6
target BS ACKs back to source BS: handover complete, source BS can release resources
7
mobile’s datagrams now flow through new tunnel from target BS to UPF
5
Mobility in 5G networks: handover

## Slide 136: Handover: timeline, signaling
AMF
Access, Mobility
Management
SMF
Session
Management
UPF
User Plane Function
device
source base station
target base station
detach from source base station, attach to target base station
device data
buffer device data from source base station
RRC reconfig.
complete
handover
success
handover
in the
RAN
transfer
status
path switch req.
PDU session
update
session mod.
req/response
data end marker
device data
device data
path switch req. ACK
PDU session
update resp.
device context
release
handover
in the
Core
measurement
handover
request
handover
request ACK
RRC
reconfig.
transfer
status
device data
device data
accept?
making
handover
decision
time

## Slide 137: Chapter 7 outline
introduction
radio: the physical layer
the wireless access network
  principles, WiFi, 5G
the wireless core network
  principles, 5G
mobility
Bluetooth, satellite, IoT wireless networks

## Slide 138: Bluetooth (BT) overview
example of wireless ad hoc network: devices have no “infrastructure” (e.g., access point, base station) to connect to
BT devices must find other BT devices, organize themselves into a network from scratch!
  connect devices at link layer, providing channel allocation
  addressing assignment
  service discovery
  application-to-application communication over Bluetooth network
  security
An entirely new architecture and protocol stack (different from Internet) is needed!
Notes: So stress that this is interesting and new!

## Slide 139: Bluetooth: overview
Bluetooth network: piconet
coverage: generally <10 m diameter
no more than 8 devices per piconet
  device initially forming network: central role
  up to 7 more devices: peripheral role
communication only between central and peripheral node
  no direct peripheral-to-peripheral communication
BT device has unique 48-bit address
Operate in unlicensed ISM band: 2.4 GHz
C
P
device with central role
device with peripheral role
diameter of
coverage
C
P
P
P

## Slide 140: Bluetooth basics: wireless channel
operates in 2.4-2.5 GHz ISM radio band
  Classic BT: 1 MHz bandwidth/channel, 79 channels, 2.1 Mbit network max rate
  BLE: 2 MHz bandwidth/channel, 40 channels. 3 advertising, 37 data channels
BT channel: TDM, 625 msec slot length
channel access via polling: central device advertises, grants channel access to peripherals in its BT network
uses frequency hopping (form of “spread spectrum”) transmissions
C
P
device with central role
device with peripheral role
diameter of
coverage
C
P
P
P

## Slide 141: Bluetooth channel: frequency hopping
senders in BT network “hop” among 79 frequencies/channels
  transmit on different frequency after each slot
  hopping pattern known by all BT devices in same piconet
different BT piconets (with different hop patterns) can exist in same space
Q: Why hop?
A: minimize effects of interference:
potentially many interfering transmitters in ISM
If interfering device uses channel x, x occurs only occasionally in sequence
BT frame sent on x (not received at receive due to interference), retransmitted on different frequency in next slot
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
625 msec
slot
channel #
1
2
3
4
76
77
78
79
time
Hopping pattern used by BT network 1
Hopping pattern used by BT network 2
Notes: Top half of slide is about what hopping is, but why hop in the first place?

## Slide 142: Bluetooth architecture, protocol stack (simplified)
Bluetooth stack completely different from Internet stack!
  differences reflect BT’s special purpose
no “network,” “transport” layer!
  no routing in Classic BT (BLE adds managed flooding)
layers not as conceptually well-defined as in Internet, 5G
Applications,
E2E services
Logical Link Control and Adaptation (L2CAP)
physical
link
Classic
BLE
Host (OS)
Controller
(firmware)
separate controllers for classic, BLE
Host-Controller
Interface (HCI)
host, controller structure deeply embedded in architecture
Notes: Probably the best picture in the Bluetooth Spec is Figure 2.1 in 5.0 specification (“Figure 2.1: Bluetooth core system architecture”). But it’s really complicated and there isn’t really clear layering.

## Slide 143: Logical Link Control, Adaptation (L2CAP) layer
creation, management of end-end L2CAP channels between two devices
  channels for E2E application/user data, or higher-level services
  reliability, flow control, segmentation
L2CAP channels types:
  connection-oriented, asynchronous (ACL)
  connectionless, asynchronous (ACL)
  synchronous (eSCO), e.g., for periodic audio app)
Notes: Note that description/layer of link controller (which is really the lower sublayer) and link manager in Sauter’s book is incorrect.

## Slide 144: Bluetooth piconet and L2CAP connections
Bluetooth central role
physical
link
L2CAP
MP3
music
MP3
music
Bluetooth peripheral
physical
link
L2CAP
Bluetooth peripheral
Bluetooth piconet wireless
channel (frequency hopping)
Service
discovery
Service
discovery
Remote
keyboard
Service
discovery
Remote
keyboard
L2CAP
link
physical
end-to-end L2CAP connections
Notes: Note that description/layer of link controller (which is really the lower sublayer) and link manager in Sauter’s book is incorrect.

## Slide 145: Satellite applications
Sensing:
environment: weather, land use, various human activity
resolution: ~m/pixel
Broadcast:
consumer: Direct to Home TV/video, radio (Dish, SiriusXM)
business: content to many cable head ends
GPS
leverage broadcast: one send reaches many users
Internet:
connectivity to unserved regions, alternative to wired Internet
low latency over long distances
access in airplanes

## Slide 146: GEO and LEO satellites
GEO:
geosynchonous: stationary with respect to ground
35,768 km above earth
~800 msec RTT
wide area coverage / satellite
LEO:
Low Earth Orbit: satellite moves with respect to ground: 27,000 km/hour
  within line of sight (LOS) of ground station for 5-15 mins
550 - 1200 km above earth
~30 msec RTT in practice
smaller area coverage / satellite
  constellation (network) of multiple LEO satellites to cover wide area
  inter-satellite links (ISL)

## Slide 147: Satellites: why all the fuss?
Sources: A. Raman, LEO Satellite Mega Constellations, networkingchannel.eu;
N.Pachler et al., An Updated Comparison of Four Low Earth Orbit Satellite Constellation Systems to Provide Global Broadband; company literature
Lots of (LEOS) satellites being launched
LEOS constellations
 | # deployed (2025) | # planned | ISL planned?
Starlink | 7,239 | 12,000 - 42,000 | Yes
EutelSat Oneweb | 648 | 716 – 6,372 | No
Kuipers (Amazon) | 27 | 3,236 | ?
Telesat | 1 | 298 - 1671 | Yes
Notes: Source: A. Raman, LEO Satellite Mega, networkingchannel.eu

## Slide 148: Components of a LEO satellite network
LEO satellites in motion
rural,
remote
communications
airborne,
maritime
vehicles
intersatellite links (ISL)
satellite channel
Broadcast (multicast) down
unicast up
“footprint”
ground
stations
Internet
mobile user terminals
Starlink satellite dish: “Dishy McFlatface”

## Slide 149: Satellite networking: a link or a network?
links in the sky
single satellite hop between base stations
AKA “bent pipe” architecture
network in the sky:
multiple satellite hops between base stations
routing among satellites

## Slide 150
Starlink
April 2025: ~7,239 operational LEO satellites (planned: 12K, requesetd:30K)
  first launches: 2019
  three low-Earth-orbit orbital shells, at 525, 530, 535 km
  satellites: 500 – 2700 lbs
services:
  Internet service: 4M subscribers in Sept 2024 (residential US: $120/mo)
  service in Ukraine (terrestrial networks damaged)
  2024: testing direct-to-smartphone tests would use cellular spectrum from SpaceX’s U.S. mobile partner T-Mobile

## Slide 151: IoT: many, many use cases!
Monitoring: pressure, vibration, 3D tilt, temperature, humidity, switches, openings, battery charge, voltage, leaks, cracks, strain gauges, fill levels ...
Asset geolocation, tracking warehouse security, monitoring transport conditions, e.g., for food safety ...
Monitoring: sound, air, water, weather, lighting, traffic, crowds, infrastrcuture; sharing (bikes) ...
Smart metering, service (de)activation , efficiency monitoring, remote diagnosis, asset surveillance, quality monitoring ...
rainfall, temperature, wind, humidity, animal tracking and health, soil condition, infrastructure monitoring ...
Security, enviro conditions (temp., air, lights, power), predictive infrastructure monitoring, ...
.... and there’s many more!
Notes: Summarized from https://www.sigfox.com/

## Slide 152: Lots of connected IoT devices, and more soon!
https://www.statista.com/statistics/512650/worldwide-connected-devices-amount/
IoT
PC, laptops,
tablets, phones
number of devices (in billions)
60
50
40
30
20
10
2014
2028

## Slide 153: IoT communication requirements
wireless
distance: from meters to kilometers
data rate: 100’s bps when active (metering) to ~1 Mbps (video surveillance)
energy: always a consideration
  up ~10 years without external power
  local energy harvesting
wide area coverage
high data rate
low energy consumption
short
range: WiFi,
BLE, Zigbee
traditional
Cellular:
4/5G
low power
wide area:
LoRaWAN,
LTE-M
IoT technical tradeoffs
Notes: So stress that this is interesting and new!

## Slide 154: Wireless and mobile networks: Summary
The physical layer: radio
The wireless access network
  principles, WiFi, 5G
The wireless core network
  principles, 5G
Mobility
Bluetooth, satellite, IoT wireless networks
For a more extensive treatment of wireless and mobile networks visit: https://gaia.cs.umass.edu/wireless_and_mobile_networks