## Slide 1
Chapter 2 Application Layer
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2025
J.F Kurose and K.W. Ross, All Rights Reserved
Computer Networking: A Top-Down Approach 9th edition Jim Kurose, Keith Ross Pearson, 2025
Notes: Version 9.0: updated to 9th Edition, June 2025

## Slide 2: Application layer: overview
Principles of network applications
Web and HTTP
E-mail, SMTP, IMAP
The Domain Name System DNS
video streaming and content distribution networks
socket programming with UDP and TCP

## Slide 3: Application layer: overview
Our goals:
conceptual and implementation aspects of application-layer protocols
  transport-layer service models
  client-server paradigm
  peer-to-peer paradigm
learn about protocols by examining popular application-layer protocols and infrastructure
  HTTP
  SMTP, IMAP
  DNS
  video streaming systems, CDNs
programming network applications
  socket API

## Slide 4: Some network apps
social media
Web
text messaging
e-mail
multi-user network games
streaming stored video (YouTube, Hulu, Netflix)
P2P file sharing
voice over IP
real-time video conferencing (e.g., Zoom)
Internet search
remote login
…
Q: your favorites?

## Slide 5: Creating a network app
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
write programs that:
run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
no need to write software for network-core devices
network-core devices do not run user applications
applications on end systems allows for rapid app development, propagation

## Slide 6: Client-server paradigm
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
server:
always-on host
permanent IP address
often in data centers, for scaling
clients:
contact, communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other
examples: HTTP, IMAP, FTP

## Slide 7: Peer-peer architecture
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
no always-on server
arbitrary end systems directly communicate
peers request service from other peers, provide service in return to other peers
  self scalability – new peers bring new service capacity, as well as new service demands
peers are intermittently connected and change IP addresses
  complex management
example: P2P file sharing [BitTorrent]

## Slide 8: Processes communicating
process: program running within a host
within same host, two processes communicate using inter-process communication (defined by OS)
processes in different hosts communicate by exchanging messages
note: applications with P2P architectures have client processes & server processes
client process: process that initiates communication
server process: process that waits to be contacted
clients, servers

## Slide 9: Sockets
process sends/receives messages to/from its socket
socket analogous to door
  sending process shoves message out door
  sending process relies on transport infrastructure on other side of door to deliver message to socket at receiving process
  two sockets involved: one on each side
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 10: Addressing processes
to receive messages, process must have identifier
host device has unique 32-bit IP address
Q: does IP address of host on which process runs suffice for identifying the process?
identifier includes both IP address and port numbers associated with process on host.
example port numbers:
  HTTP server: 80
  mail server: 25
to send HTTP message to gaia.cs.umass.edu web server:
  IP address: 128.119.245.12
  port number: 80
more shortly…
  A: no, many processes can be running on same host

## Slide 11: An application-layer protocol defines:
types of messages exchanged,
  e.g., request, response
message syntax:
  what fields in messages & how fields are delineated
message semantics
  meaning of information in fields
rules for when and how processes send & respond to messages
open protocols:
defined in RFCs, everyone has access to protocol definition
allows for interoperability
e.g., HTTP, SMTP
proprietary protocols:
e.g., Zoom

## Slide 12: What transport service does an app need?
data integrity
some apps (e.g., file transfer, web transactions) require 100% reliable data transfer
other apps (e.g., audio) can tolerate some loss
timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
security
encryption, data integrity, …

## Slide 13: Transport service requirements: common apps
application
file transfer/download
e-mail
Web documents
real-time audio/video
streaming audio/video
interactive games
text messaging
data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
throughput
elastic
elastic
elastic
audio: 5Kbps-1Mbps
video:10Kbps-5Mbps
same as above
Kbps+
elastic
time sensitive?
no
no
no
yes, 10’s msec
yes, few secs
yes, 10’s msec
yes and no

## Slide 14: Internet transport protocols services
TCP service:
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
connection-oriented: setup required between client and server processes
does not provide: timing, minimum throughput guarantee, security
UDP service:
unreliable data transfer between sending and receiving process
does not provide: reliability, flow control, congestion control, timing, throughput guarantee, security, or connection setup.
Q: why bother? Why is there a UDP?

## Slide 15: Internet applications, and transport protocols
application
file transfer/download
e-mail
Web documents
Internet telephony
streaming audio/video
interactive games
application
layer protocol
FTP [RFC 959]
SMTP [RFC 5321]
HTTP [RFC 7230, 9110]
SIP [RFC 3261], RTP [RFC 3550], or proprietary HTTP [RFC 7230], DASH
WOW, FPS (proprietary)
transport protocol
TCP
TCP
TCP
TCP or UDP
TCP
UDP or TCP

## Slide 16: Securing TCP
Vanilla TCP & UDP sockets:
no encryption
cleartext passwords sent into socket traverse Internet in cleartext (!)
Transport Layer Security (TLS)
provides encrypted TCP connections
data integrity
end-point authentication
TLS implemented in application layer
apps use TLS libraries, that use TCP in turn
  cleartext sent into “socket” traverse Internet encrypted
  more: Chapter 8

## Slide 17: Application layer: overview
Principles of network applications
Web and HTTP
E-mail, SMTP, IMAP
The Domain Name System DNS
video streaming and content distribution networks
socket programming with UDP and TCP

## Slide 18: Web and HTTP
First, a quick review…
web page consists of objects, each of which can be stored on different Web servers
object can be HTML file, JPEG image, Java applet, audio file,…
web page consists of base HTML-file which includes several referenced objects, each addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 19: HTTP overview
HTTP: hypertext transfer protocol
Web’s application-layer protocol
client/server model:
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
HTTP request
HTTP response
HTTP request
HTTP response
iPhone running
Safari browser
PC running
Firefox browser
server running
Apache Web
server

## Slide 20: HTTP overview (continued)
HTTP uses TCP:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 21: HTTP connections: two types
Non-persistent HTTP
TCP connection opened
at most one object sent over TCP connection
TCP connection closed
downloading multiple objects required multiple connections
Persistent HTTP
TCP connection opened to a server
multiple objects can be sent over single TCP connection between client, and that server
TCP connection closed

## Slide 22: Non-persistent HTTP: example
User enters URL:
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80 “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(containing text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index

## Slide 23: Non-persistent HTTP: example (cont.)
User enters URL:
(containing text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index
5. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.
time

## Slide 24: Non-persistent HTTP: response time
RTT (definition): time for a small packet to travel from client to server and back
HTTP response time (per object):
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
object/file transmission time
time to
transmit
file
initiate TCP
connection
RTT
request file
RTT
file received
time
time
Non-persistent HTTP response time = 2RTT+ file transmission time

## Slide 25: Persistent HTTP (HTTP 1.1)
Non-persistent HTTP issues:
requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open multiple parallel TCP connections to fetch referenced objects in parallel
Persistent HTTP (HTTP1.1):
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects (cutting response time in half)

## Slide 26: HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
header
lines
GET /index.html HTTP/1.1\r\n
Host: www-net.cs.umass.edu\r\n
User-Agent: Mozilla/5.0 (Macintosh; Intel Mac OS X 10.15; rv:80.0) Gecko/20100101 Firefox/80.0 \r\n
Accept: text/html,application/xhtml+xml\r\n
Accept-Language: en-us,en;q=0.5\r\n
Accept-Encoding: gzip,deflate\r\n
Connection: keep-alive\r\n
\r\n
carriage return character
line-feed character
request line (GET, POST,
HEAD commands)
carriage return, line feed at start of line indicates end of header lines
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 27: HTTP request message: general format
request
line
header
lines
body
method
sp
sp
cr
lf
version
URL
cr
lf
value
header field name
cr
lf
value
header field name
~
~
~
~
cr
lf
entity body
~
~
~
~

## Slide 28: Other HTTP request messages
POST method:
web page often includes form input
user input sent from client to server in entity body of HTTP POST request message
GET method (for sending data to server):
include user data in URL field of HTTP GET request message (following a ‘?’):
www.somesite.com/animalsearch?monkeys&banana
HEAD method:
requests headers (only) that would be returned if specified URL were requested with an HTTP GET method.
PUT method:
uploads new file (object) to server
completely replaces file that exists at specified URL with content in entity body of POST HTTP request message

## Slide 29: HTTP response message
status line (protocol
status code status phrase)
header
lines
data, e.g., requested
HTML file
HTTP/1.1 200 OK
Date: Tue, 08 Sep 2020 00:53:20 GMT
Server: Apache/2.4.6 (CentOS) OpenSSL/1.0.2k-fips PHP/7.4.9 mod_perl/2.0.11 Perl/v5.16.3
Last-Modified: Tue, 01 Mar 2016 18:57:50 GMT
ETag: "a5b-52d015789ee9e"
Accept-Ranges: bytes
Content-Length: 2651
Content-Type: text/html; charset=UTF-8
\r\n
data data data data data ...
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 30: HTTP response status codes
200 OK
  request succeeded, requested object later in this message
301 Moved Permanently
  requested object moved, new location specified later in this message (in Location: field)
400 Bad Request
  request msg not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
status code appears in 1st line in server-to-client response message.
some sample codes:

## Slide 31: Trying out HTTP (client side) for yourself
1. netcat to your favorite Web server:
opens TCP connection to port 80 (default HTTP server port) at gaia.cs.umass.edu.
anything typed in will be sent to port 80 at gaia.cs.umass.edu
3. look at response message sent by HTTP server!
(or use Wireshark to look at captured HTTP request/response)
2. type in a GET HTTP request:
GET /kurose_ross/interactive/index.php HTTP/1.1
Host: gaia.cs.umass.edu
by typing this in (hit carriage return twice), you send this minimal (but complete) GET request to HTTP server
% nc -c -v gaia.cs.umass.edu 80 (for Mac)
>ncat –C gaia.cs.umass.edu 80 (for Windows)

## Slide 32: Maintaining user/server state: cookies
Recall: HTTP GET/response interaction is stateless
no notion of multi-step exchanges of HTTP messages to complete a Web “transaction”
  no need for client/server to track “state” of multi-step exchange
  all HTTP requests are independent of each other
  no need for client/server to “recover” from a partially-completed-but-never-completely-completed transaction
a stateful protocol: client makes two changes to X, or none at all
time
time
OK
OK
unlock X
OK
update X X’
update X X’’
lock data record X
OK
X
X
X’
X’’
X’’
t’
Q: what happens if network connection or client crashes at t’ ?
Notes: t’

## Slide 33: Maintaining user/server state: cookies
Web sites and client browser use cookies to maintain some state between transactions
four components:
  1) cookie header line of HTTP response message
  2) cookie header line in next HTTP request message
  3) cookie file kept on user’s host, managed by user’s browser
  4) back-end database at Web site
Example:
Susan uses browser on laptop, visits specific e-commerce site for first time
when initial HTTP requests arrives at site, site creates:
  unique ID (aka “cookie”)
  entry in backend database for ID
subsequent HTTP requests from Susan to this site will contain cookie ID value, allowing site to “identify” Susan
Notes: t’

## Slide 34: Maintaining user/server state: cookies
client
Amazon server
usual HTTP response msg
usual HTTP response msg
cookie file
one week later:
usual HTTP request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
usual HTTP request msg
Amazon server
creates ID
1678 for user
create
entry
usual HTTP response
set-cookie: 1678
ebay 8734
amazon 1678
usual HTTP request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
amazon 1678
backend
database
time
time
Notes: t’

## Slide 35: HTTP cookies: comments
What cookies can be used for:
authorization
shopping carts
recommendations
user session state (Web e-mail)
cookies and privacy:
cookies permit sites to learn a lot about you on their site.
third party persistent cookies (tracking cookies) allow common identity (cookie value) to be tracked across multiple web sites
aside
Challenge: How to keep state?
at protocol endpoints: maintain state at sender/receiver over multiple transactions
in messages: cookies in HTTP messages carry state
Notes: t’

## Slide 36
Example: displaying a NY Times web page
nytimes.com
AdX.com
1
HTTP GET
2
HTTP reply
4
3
5
6
NY times page with embedded ad displayed
GET base html file from nytimes.com
1
2
fetch ad from AdX.com
4
5
display composed page
7

## Slide 37
nytimes.com (sports)
AdX.com
1634: sports, 2/15/22
NY Times: 1634
7493: NY Times sports, 2/15/22
HTTP reply
Set cookie: 1634
4
HTTP GET
Referrer: NY Times Sports
5
HTTP reply
Set cookie: 7493
HTTP
GET
AdX: 7493
Cookies: tracking a user’s browsing behavior
“first party” cookie – from website you chose to visit (provides base html file)
“third party” cookie – from website you did not choose to visit

## Slide 38
Cookies: tracking a user’s browsing behavior
nytimes.com
AdX.com
1634: sports, 2/15/22
NY Times: 1634
7493: NY Times sports, 2/15/22
AdX: 7493
socks.com
1
HTTP GET
2
HTTP reply
4
HTTP GET
Referrer: socks.com, cookie: 7493
5
HTTP reply
Set cookie: 7493
7493: socks.com, 2/16/22
AdX:
tracks my web browsing over sites with AdX ads
can return targeted ads based on browsing history

## Slide 39
Cookies: tracking a user’s browsing behavior (one day later)
nytimes.com (arts)
AdX.com
1634: sports, 2/15/22
NY Times: 1634
7493: NY Times sports, 2/15/22
AdX: 7493
socks.com
4
HTTP GET
Referrer: nytimes.com, cookie: 7493
5
HTTP reply
Set cookie: 7493
7493: socks.com, 2/16/22
cookie: 1634
HTTP reply
HTTP
GET
Set cookie: 1634
1634: arts, 2/17/22
7493: NY Times arts, 2/15/22
Returned ad for socks!

## Slide 40
Cookies: tracking a user’s browsing behavior
Cookies can be used to:
track user behavior on a given website (first party cookies)
track user behavior across multiple websites (third party cookies) without user ever choosing to visit tracker site (!)
tracking may be invisible to user:
  rather than displayed ad triggering HTTP GET to tracker, could be an invisible link
third party tracking via cookies:
disabled by default in Firefox, Safari browsers
to be disabled in Chrome browser in 2023

## Slide 41
GDPR (EU General Data Protection Regulation) and cookies
“Natural persons may be associated with online identifiers […] such as internet protocol addresses, cookie identifiers or other identifiers […].
This may leave traces which, in particular when combined with unique identifiers and other information received by the servers, may be used to create profiles of the natural persons and identify them.”
GDPR, recital 30 (May 2018)
User has explicit control over whether or not cookies are allowed
when cookies can identify an individual, cookies are considered personal data, subject to GDPR personal data regulations

## Slide 42: Web caches
user configures browser to point to a (local) Web cache
browser sends all HTTP requests to cache
  if object in cache: cache returns object to client
  else cache requests object from origin server, caches received object, then returns object to client
Goal: satisfy client requests without involving origin server
client
Web
cache
client
HTTP request
HTTP response
HTTP request
HTTP request
origin
server
HTTP response
HTTP response
Notes: t’

## Slide 43: Web caches (aka proxy servers)
Web cache acts as both client and server
  server for original requesting client
  client to origin server
Why Web caching?
reduce response time for client request
  cache is closer to client
reduce traffic on an institution’s access link
Internet is dense with caches
  enables “poor” content providers to more effectively deliver content
server tells cache about object’s allowable caching in response header:
Notes: re: poor content providers – like in real-estate, location is everything. servers want to be close to clients.

## Slide 44: Caching example
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
Performance:
access link utilization = .97
LAN utilization: .0015
end-end delay = Internet delay +
access link delay + LAN delay
= 2 sec + minutes + usecs
Scenario:
access link rate: 1.54 Mbps
RTT from institutional router to server: 2 sec
web object size: 100K bits
average request rate from browsers to origin servers: 15/sec
  avg data rate to browsers: 1.50 Mbps
problem: large queueing delays at high utilization!
Notes: explain why minutes (recall earlier delay versus arrival rate curve from Chapter 1)

## Slide 45: Option 1: buy a faster access link
Performance:
access link utilization = .97
LAN utilization: .0015
end-end delay = Internet delay +
access link delay + LAN delay
= 2 sec + minutes + usecs
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
Scenario:
access link rate: 1.54 Mbps
RTT from institutional router to server: 2 sec
web object size: 100K bits
average request rate from browsers to origin servers: 15/sec
  avg data rate to browsers: 1.50 Mbps
154 Mbps
154 Mbps
.0097
msecs
Cost: faster access link (expensive!)
Notes: t’

## Slide 46: Option 2: install a web cache
Performance:
LAN utilization: .?
access link utilization = ?
average end-end delay = ?
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
Scenario:
access link rate: 1.54 Mbps
RTT from institutional router to server: 2 sec
web object size: 100K bits
average request rate from browsers to origin servers: 15/sec
  avg data rate to browsers: 1.50 Mbps
How to compute link
utilization, delay?
Cost: web cache (cheap!)
local web cache
Notes: t’

## Slide 47: Calculating access link utilization, end-end delay with cache:
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
local web cache
suppose cache hit rate is 0.4:
40% requests served by cache, with low (msec) delay
60% requests satisfied at origin
  rate to browsers over access link
  = 0.6 * 1.50 Mbps = .9 Mbps
  access link utilization = 0.9/1.54 = .58 means low (msec) queueing delay at access link
average end-end delay:
  = 0.6 * (delay from origin servers)
  + 0.4 * (delay when satisfied at cache)
  = 0.6 (2.01) + 0.4 (~msecs) = ~ 1.2 secs
lower average end-end delay than with 154 Mbps link (and cheaper too!)
Notes: t’

## Slide 48: Browser caching: Conditional GET
Goal: don’t send object if browser has up-to-date cached version
  no object transmission delay (or use of network resources)
client: specify date of browser-cached copy in HTTP request
  If-modified-since: <date>
server: response contains no object if browser-cached copy is up-to-date:
  HTTP/1.0 304 Not Modified
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0
304 Not Modified
object
not
modified
before
<date>
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0 200 OK
<data>
object
modified
after
<date>
client
server
Notes: t’

## Slide 49: HTTP/2
Key goal: decreased delay in multi-object HTTP requests
HTTP1.1: introduced multiple, pipelined GETs over single TCP connection
server responds in-order (FCFS: first-come-first-served scheduling) to GET requests
with FCFS, small object may have to wait for transmission (head-of-line (HOL) blocking) behind large object(s)
loss recovery (retransmitting lost TCP segments) stalls object transmission
Notes: t’

## Slide 50: HTTP/2
HTTP/2: [RFC 7540, 2015] increased flexibility at server in sending objects to client:
methods, status codes, most header fields unchanged from HTTP 1.1
transmission order of requested objects based on client-specified object priority (not necessarily FCFS)
push unrequested objects to client
divide objects into frames, schedule frames to mitigate HOL blocking
Key goal: decreased delay in multi-object HTTP requests
Notes: t’

## Slide 51: HTTP/2: mitigating HOL blocking
HTTP 1.1: client requests 1 large object (e.g., video file) and 3 smaller objects
client
server
GET O1
GET O2
GET O3
GET O4
O1
O2
O3
O4
object data requested
O1
O2
O3
O4
objects delivered in order requested: O2, O3, O4 wait behind O1
Notes: t’

## Slide 52: HTTP/2: mitigating HOL blocking
HTTP/2: objects divided into frames, frame transmission interleaved
client
server
GET O1
GET O2
GET O3
GET O4
O2
O4
object data requested
O1
O2
O3
O4
O2, O3, O4 delivered quickly, O1 slightly delayed
O3
O1
Notes: shortest job first: decreased average delay!

## Slide 53: HTTP/2 to HTTP/3
HTTP/2 over single TCP connection means:
recovery from packet loss still stalls all object transmissions
  as in HTTP 1.1, browsers have incentive to open multiple parallel TCP connections to reduce stalling, increase overall throughput
no security over vanilla TCP connection
HTTP/3: adds security, per object error- and congestion-control (more pipelining) over UDP
Notes: t’

## Slide 54: QUIC: Quick UDP Internet Connections
application-layer protocol, on top of UDP
  increase performance of HTTP
  deployed on many Google servers, apps (Chrome, mobile YouTube app)
IP
TCP
TLS
HTTP/2
IP
UDP
QUIC
HTTP/2 (slimmed)
Network
Transport
Application
HTTP/2 over TCP
HTTP/3
HTTP/2 over QUIC over UDP

## Slide 55: QUIC: Quick UDP Internet Connections
adopts approaches we’ll study in chapter for connection establishment, error control, congestion control
  error and congestion control: “Readers familiar with TCP’s loss detection and congestion control will find algorithms here that parallel well-known TCP ones.” [from QUIC specification]
  connection establishment: reliability, congestion control, authentication, encryption, state established in one RTT

## Slide 56: QUIC: Connection establishment
TCP handshake
(transport layer)
TLS handshake
(security)
TCP (reliability, congestion control state) + TLS (authentication, crypto state)
2 serial handshakes
data
data
QUIC: reliability, congestion control, authentication, crypto state
1 handshake
QUIC
1RTT handshake

## Slide 57: QUIC: 0-RTT Connection establishment
data
TLS session ticket sent by server, cached at client
end of first QUIC connection
start of second QUIC connection
Client uses last session ticket for encryption, authentication for new connection
0 RTT handshake delay
data

## Slide 58: Application layer: overview
Principles of network applications
Web and HTTP
E-mail, SMTP, IMAP
The Domain Name System DNS
video streaming and content distribution networks
socket programming with UDP and TCP

## Slide 59: E-mail
Three major components:
user agents
mail servers
simple mail transfer protocol: SMTP
User Agent
a.k.a. “mail reader”
composing, editing, reading mail messages
e.g., Outlook, iPhone mail client
outgoing, incoming messages stored on server
user mailbox
outgoing
message queue
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent

## Slide 60: E-mail: mail servers
user mailbox
outgoing
message queue
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent
mail servers:
mailbox contains incoming messages for user
message queue of outgoing (to be sent) mail messages
SMTP protocol between mail servers to send email messages
client: sending mail server
“server”: receiving mail server

## Slide 61: SMTP RFC (5321)
uses TCP to reliably transfer email message from client (mail server initiating connection) to server, port 25
  direct transfer: sending server (acting like client) to receiving server
three phases of transfer
  SMTP handshaking (greeting)
  SMTP transfer of messages
  SMTP closure
command/response interaction (like HTTP)
  commands: ASCII text
  response: status code and phrase
initiate TCP
connection
RTT
time
220
250 Hello
HELO
SMTP handshaking
TCP connection
initiated
“client”
SMTP server
“server”
SMTP server
SMTP transfers

## Slide 62: Scenario: Alice sends e-mail to Bob
1) Alice uses UA to compose e-mail message “to” bob@someschool.edu
4) SMTP client sends Alice’s message over the TCP connection
user
agent
mail
server
mail
server
1
2
3
4
5
6
Alice’s mail server
Bob’s mail server
user
agent
2) Alice’s UA sends message to her mail server using SMTP; message placed in message queue
3) client side of SMTP at mail server opens TCP connection with Bob’s mail server
5) Bob’s mail server places the message in Bob’s mailbox
6) Bob invokes his user agent to read message

## Slide 63: Sample SMTP interaction
S: 220 hamburger.edu
C: HELO crepes.fr
S: 250 Hello crepes.fr, pleased to meet you
C: MAIL FROM: <alice@crepes.fr>
S: 250 alice@crepes.fr... Sender ok
C: RCPT TO: <bob@hamburger.edu>
S: 250 bob@hamburger.edu ... Recipient ok
C: DATA
S: 354 Enter mail, end with "." on a line by itself
C: Do you like ketchup?
C: How about pickles?
C: .
S: 250 Message accepted for delivery
C: QUIT
S: 221 hamburger.edu closing connection

## Slide 64: SMTP: observations
SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
SMTP server uses CRLF.CRLF to determine end of message
comparison with HTTP:
HTTP: client pull
SMTP: client push
both have ASCII command/response interaction, status codes
HTTP: each object encapsulated in its own response message
SMTP: multiple objects sent in multipart message

## Slide 65: Mail message format
SMTP: protocol for exchanging e-mail messages, defined in RFC 5321 (like RFC 7231 defines HTTP)
RFC 2822 defines syntax for e-mail message itself (like HTML defines syntax for web documents)
header
body
blank
line
header lines, e.g.,
  To:
  From:
  Subject:
  these lines, within the body of the email message area different from SMTP MAIL FROM:, RCPT TO: commands!
Body: the “message” , ASCII characters only

## Slide 66: Retrieving email: mail access protocols
sender’s e-mail
server
SMTP
SMTP
receiver’s e-mail
server
e-mail access
protocol
(e.g., IMAP, HTTP)
user
agent
user
agent
SMTP: delivery/storage of e-mail messages to receiver’s server
mail access protocol: retrieval from server
  IMAP: Internet Mail Access Protocol [RFC 3501]: messages stored on server, IMAP provides retrieval, deletion, folders of stored messages on server
HTTP: gmail, Hotmail, Yahoo!Mail, etc. provides web-based interface on top of STMP (to send), IMAP (or POP) to retrieve e-mail messages

## Slide 67: Application Layer: Overview
Principles of network applications
Web and HTTP
E-mail, SMTP, IMAP
The Domain Name System DNS
video streaming and content distribution networks
socket programming with UDP and TCP

## Slide 68: DNS: Domain Name System
people: many identifiers:
  SSN, name, passport #
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams
  “name”, e.g., cs.umass.edu - used by humans
Q: how to map between IP address and name, and vice versa ?
Domain Name System (DNS):
distributed database implemented in hierarchy of many name servers
application-layer protocol: hosts, DNS servers communicate to resolve names (address/name translation)
  note: core Internet function, implemented as application-layer protocol
  complexity at network’s “edge”

## Slide 69: DNS: services, structure
Q: Why not centralize DNS?
single point of failure
traffic volume
distant centralized database
maintenance
DNS services:
hostname-to-IP-address translation
host aliasing
  canonical, alias names
mail server aliasing
load distribution
  replicated Web servers: many IP addresses correspond to one name
A: doesn‘t scale!
Comcast DNS servers alone: 600B DNS queries/day
Akamai DNS servers alone: 2.2T DNS queries/day

## Slide 70: Thinking about the DNS
humongous distributed database:
~ billion records, each simple
handles many trillions of queries/day:
many more reads than writes
performance matters: almost every Internet transaction interacts with DNS - msecs count!
organizationally, physically decentralized:
millions of different organizations responsible for their records
“bulletproof”: reliability, security

## Slide 71: DNS: a distributed, hierarchical database
Client wants IP address for www.amazon.com; 1st approximation:
client queries root server to find .com DNS server
client queries .com DNS server to get amazon.com DNS server
client queries amazon.com DNS server to get IP address for www.amazon.com
.com DNS servers
.org DNS servers
.edu DNS servers
…
…
Top Level Domain
Root DNS Servers
Root
nyu.edu
DNS servers
umass.edu
DNS servers
yahoo.com
DNS servers
amazon.com
DNS servers
pbs.org
DNS servers
Authoritative
…
…
…
…

## Slide 72: DNS: root name servers
official, contact-of-last-resort by name servers that can not resolve name

## Slide 73: DNS: root name servers
official, contact-of-last-resort by name servers that can not resolve name
incredibly important Internet function
  Internet couldn’t function without it!
  DNSSEC – provides security (authentication, message integrity)
13 logical root name “servers” worldwide; each “server,” replicated many times
ICANN (Internet Corporation for Assigned Names and Numbers) manages root DNS domain
ICANN (Internet Corporation for Assigned Names and Numbers) manages root DNS domain

## Slide 74: Top-Level Domain, and authoritative servers
Top-Level Domain (TLD) servers:
  responsible for .com, .org, .net, .edu, .aero, .jobs, .museums, and all top-level country domains, e.g.: .cn, .uk, .fr, .ca, .jp
  Network Solutions: authoritative registry for .com, .net TLD
  Educause: .edu TLD
authoritative DNS servers:
  organization’s own DNS server(s), providing authoritative hostname to IP mappings for organization’s named hosts
  can be maintained by organization or service provider

## Slide 75: Local DNS name servers
when host makes DNS query, it is sent to its local DNS server
  Local DNS server returns reply, answering:
    from its local cache of recent name-to-address translation pairs (possibly out of date!)
    forwarding request into DNS hierarchy for resolution
  each ISP has local DNS name server; to find yours:
    MacOS: % scutil --dns
    Windows: >ipconfig /all
local DNS server doesn’t strictly belong to hierarchy

## Slide 76: DNS name resolution: iterated query
Example: host at engineering.nyu.edu wants IP address for gaia.cs.umass.edu
Iterated query:
contacted server replies with name of server to contact
“I don’t know this name, but ask this server”
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.nyu.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server

## Slide 77: DNS name resolution: recursive query
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.nyu.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Recursive query:
puts burden of name resolution on contacted name server
heavy load at upper levels of hierarchy?
Example: host at engineering.nyu.edu wants IP address for gaia.cs.umass.edu

## Slide 78: Basic Domain Name Resolution
Translates domain names into IP addresses
Every host knows a local DNS server
  Sends all queries to the local DNS server
If the local DNS can answer the query, then you’re done
  Local server is also the authoritative server for that name
  Local server has cached the record for that name
Otherwise, go down the hierarchy and search for the authoritative name server (root)
  Every local DNS server knows the root servers
  Use cache to skip steps if possible
    e.g. skip the root and go directly to .edu if the root file is cached

## Slide 79: DNS Resolution
242.66.45.4

## Slide 80: Local Name Servers
Northeastern
Each ISP/company has a local, default name server
Often configured via DHCP
Hosts begin DNS queries by contacting the local name server
Frequently cache query results
Where is google.com?

## Slide 81: Authoritative Name Servers
Stores the nameIP mapping for a given host
Northeastern
Where is www.neu.edu?
Root
edu
neu
www.neu.edu
Authority for ‘neu.edu’
www.neu.edu = 155.33.17.68
Authority for ‘edu’

## Slide 82: The Importance of DNS
The goal of DNS is relatively simple -- in general, words are easier for people to remember than long, confusing number sequences.
Without DNS…
  How could you get to any websites?
Your mailserver
  When you sign up for websites, you use your email address
  What if someone hijacks the DNS for your mail server?
DNS is the root of trust for the web
  When a user types www.bankofamerica.com, they expect to be taken to their bank’s website
  What if the DNS record is compromised?

## Slide 83: Caching DNS Information
once (any) name server learns mapping, it caches mapping, and immediately returns a cached mapping in response to a query
  caching improves response time
  cache entries timeout (disappear) after some time (TTL)
  TLD servers typically cached in local name servers
cached entries may be out-of-date
  if named host changes IP address, may not be known Internet-wide until all TTLs expire!
  best-effort name-to-address translation!

## Slide 84: DNS records
DNS: distributed database storing resource records (RR)
type=NS
  name is domain (e.g., foo.com)
  value is hostname of authoritative name server for this domain
RR format: (name, value, type, ttl)
type=A
  name is hostname
  value is IP address
type=CNAME
  name is alias name for some “canonical” (the real) name
  www.ibm.com is really servereast.backup2.ibm.com
  value is canonical name
type=MX
  value is name of SMTP mail server associated with name

## Slide 85: DNS records
RR format: (name, value, type, ttl)

## Slide 86: DNS protocol messages
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes
DNS query and reply messages, both have same format:
message header:
identification: 16 bit # for query, reply to query uses same #
flags:
  query or reply
  recursion desired
  recursion available
  reply is authoritative

## Slide 87: DNS protocol messages
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes
DNS query and reply messages, both have same format:
name, type fields for a query
RRs in response to query
records for authoritative servers
additional “ helpful” info that may be used

## Slide 88: Getting your info into the DNS
example: new startup “Network Utopia”
register name networkuptopia.com at DNS registrar (e.g., Network Solutions)
  provide names, IP addresses of authoritative name server (primary and secondary)
  registrar inserts NS, A RRs into .com TLD server:
  (networkutopia.com, dns1.networkutopia.com, NS)
  (dns1.networkutopia.com, 212.212.212.1, A)
create authoritative server locally with IP address 212.212.212.1
  type A record for www.networkuptopia.com
  type MX record for networkutopia.com

## Slide 89: DNS security
DDoS attacks
bombard root servers with traffic
  not successful to date
  traffic filtering
  local DNS servers cache IPs of TLD servers, allowing root server bypass
bombard TLD servers
  potentially more dangerous
Spoofing attacks
intercept DNS queries, returning bogus replies
  DNS cache poisoning
  RFC 4033: DNSSEC authentication services

## Slide 90: Application layer: overview
Principles of network applications
Web and HTTP
E-mail, SMTP, IMAP
The Domain Name System DNS
P2P applications
video streaming and content distribution networks
socket programming with UDP and TCP

## Slide 91: Video Streaming and CDNs: context
stream video traffic: major consumer of Internet bandwidth
  Netflix, YouTube, Amazon Prime: 80% of residential ISP traffic (2020)
challenge: scale - how to reach ~1B users?
challenge: heterogeneity
  different users have different capabilities (e.g., wired versus mobile; bandwidth rich versus bandwidth poor)
solution: distributed, application-level infrastructure

## Slide 92: Multimedia: video
video: sequence of images displayed at constant rate
  e.g., 24 images/sec
digital image: array of pixels
  each pixel represented by bits
coding: use redundancy within and between images to decrease # bits used to encode image
  spatial (within image)
  temporal (from one image to next)
……………………..
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………….…….
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i

## Slide 93: Multimedia: video
……………………..
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………….…….
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i
CBR: (constant bit rate): video encoding rate fixed
VBR: (variable bit rate): video encoding rate changes as amount of spatial, temporal coding changes
examples:
  MPEG 1 (CD-ROM) 1.5 Mbps
  MPEG2 (DVD) 3-6 Mbps
  MPEG4 (often used in Internet, 64Kbps – 12 Mbps)

## Slide 94: Streaming stored video
Main challenges:
server-to-client bandwidth will vary over time, with changing network congestion levels (in house, access network, network core, video server)
packet loss, delay due to congestion will delay playout, or result in poor video quality
simple scenario:
video server
(stored video)
client
Internet

## Slide 95: Streaming stored video
video
recorded (e.g., 30 frames/sec)
2. video
sent
Cumulative data
streaming: at this time, client playing out early part of video, while server still sending later part of video
time
3. video received, played out at client
(30 frames/sec)
network delay
(fixed in this example)

## Slide 96: Streaming stored video: challenges
continuous playout constraint: during client video playout, playout timing must match original timing
  … but network delays are variable (jitter), so will need client-side buffer to match continuous playout constraint
other challenges:
  client interactivity: pause, fast-forward, rewind, jump through video
  video packets may be lost, retransmitted

## Slide 97: Streaming stored video: playout buffering
constant bit
rate video
transmission
Cumulative data (chunks)
time
variable
network
delay
client video
reception
constant bit
rate video
playout at client
client playout
delay
buffered
video
client-side buffering and playout delay: compensate for network-added delay, delay jitter
1
2
3
4
5
6
7
8
9
10
at t0, 6 chunks have arrived, 2 chunks have been played out, so the buffer has 4 chunks
t0

## Slide 98: Streaming multimedia: DASH
server:
  divides video file into multiple chunks
  each chunk encoded at multiple different rates
  different rate encodings stored in different files
  files replicated in various CDN nodes
  manifest file: provides URLs for different chunks
client
?
client:
  periodically estimates server-to-client bandwidth
  consulting manifest, requests one chunk at a time
    chooses maximum coding rate sustainable given current bandwidth
    can choose different coding rates at different points in time (depending on available bandwidth at time), and from different servers
...
...
...
Dynamic, Adaptive Streaming over HTTP

## Slide 99: Streaming multimedia: DASH
...
...
...
“intelligence” at client: client determines
  when to request chunk (so that buffer starvation, or overflow does not occur)
  what encoding rate to request (higher quality when more bandwidth available)
  where to request chunk (can request from URL server that is “close” to client or has high available bandwidth)
Streaming video = encoding + DASH + playout buffering
client
?

## Slide 100: Content distribution networks (CDNs)
challenge: how to stream content (selected from millions of videos) to hundreds of thousands of simultaneous users?
option 1: single, large “mega-server”
  single point of failure
  point of network congestion
  long (and possibly congested) path to distant clients
….quite simply: this solution doesn’t scale

## Slide 101: Content distribution networks (CDNs)
challenge: how to stream content (selected from millions of videos) to hundreds of thousands of simultaneous users?
  enter deep: push CDN servers deep into many access networks
    close to users
    Akamai: 240,000 servers deployed
    in > 120 countries (2015)
option 2: store/serve multiple copies of videos at multiple geographically distributed sites (CDN)
  bring home: smaller number (10’s) of larger clusters in POPs near access nets
    used by Limelight

## Slide 102: Akamai today:
Source: https://networkingchannel.eu/living-on-the-edge-for-a-quarter-century-an-akamai-retrospective-downloads/

## Slide 103: How does Netflix work?
…
…
…
…
…
…
subscriber requests content, service provider returns manifest
Netflix: stores copies of content (e.g., MADMEN) at its (worldwide) OpenConnect CDN nodes
where’s Madmen?
manifest file
  using manifest, client retrieves content at highest supportable rate
  may choose different rate or copy if network path congested
Notes: 103
Akamai: 100,000+ servers in 1000+ clusters in 1000+ networks in 70+ countries serving trillions of requests a day.
How many people use Netflix?

## Slide 104: Content distribution networks (CDNs)
…
…
…
…
…
…
Internet host-host communication as a service
OTT challenges: coping with a congested Internet from the “edge”
  what content to place in which CDN node?
  from which CDN node to retrieve content? At which rate?
OTT: “over the top”
Notes: 104
peak load: 7million viewers, 2 Tbytes via

## Slide 105: Application Layer: Overview
Principles of network applications
Web and HTTP
E-mail, SMTP, IMAP
The Domain Name System DNS
P2P applications
video streaming and content distribution networks
socket programming with UDP and TCP

## Slide 106: Socket programming
goal: learn how to build client/server applications that communicate using sockets
socket: door between application process and end-end-transport protocol
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 107: Socket programming
  Two socket types for two transport services:
  UDP: unreliable datagram
  TCP: reliable, byte stream-oriented
  Application Example:
client reads a line of characters (data) from its keyboard and sends data to server
server receives the data and converts characters to uppercase
server sends modified data to client
client receives modified data and displays line on its screen

## Slide 108: Socket programming with UDP
UDP: no “connection” between client and server:
no handshaking before sending data
sender explicitly attaches IP destination address and port # to each packet
receiver extracts sender IP address and port# from received packet
UDP: transmitted data may be lost or received out-of-order
Application viewpoint:
UDP provides unreliable transfer of groups of bytes (“datagrams”) between client and server processes

## Slide 109: Client/server socket interaction: UDP
close
clientSocket
read datagram from
clientSocket
create socket:
clientSocket =
socket(AF_INET,SOCK_DGRAM)
Create datagram with serverIP address
And port=x; send datagram via clientSocket
create socket, port= x:
serverSocket =
socket(AF_INET,SOCK_DGRAM)
read datagram from
serverSocket
write reply to
serverSocket
specifying client address,
port number
server (running on serverIP)
client

## Slide 110: Example app: UDP client
from socket import *
serverName = 'hostname'
serverPort = 12000
clientSocket = socket(AF_INET,
SOCK_DGRAM)
message = input('Input lowercase sentence:')
clientSocket.sendto(message.encode(),
(serverName, serverPort))
modifiedMessage, serverAddress =
clientSocket.recvfrom(2048)
print(modifiedMessage.decode())
clientSocket.close()
Python UDPClient
include Python’s socket library
create UDP socket
get user keyboard input
attach server name, port to message; send into socket
print out received string and close socket
read reply data (bytes) from socket
Note: this code update (2023) to Python 3
Notes: UDO and TCP code updates 3/23

## Slide 111: Example app: UDP server
Python UDPServer
from socket import *
serverPort = 12000
serverSocket = socket(AF_INET, SOCK_DGRAM)
serverSocket.bind(('', serverPort))
print('The server is ready to receive')
while True:
message, clientAddress = serverSocket.recvfrom(2048)
modifiedMessage = message.decode().upper()
serverSocket.sendto(modifiedMessage.encode(),
clientAddress)
create UDP socket
bind socket to local port number 12000
loop forever
Read from UDP socket into message, getting client’s address (client IP and port)
send upper case string back to this client
Note: this code update (2023) to Python 3

## Slide 112: Socket programming with TCP
Client must contact server
server process must first be running
server must have created socket (door) that welcomes client’s contact
Client contacts server by:
Creating TCP socket, specifying IP address, port number of server process
when client creates socket: client TCP establishes connection to server TCP
when contacted by client, server TCP creates new socket for server process to communicate with that particular client
  allows server to talk with multiple clients
  client source port # and IP address used to distinguish clients (more in Chap 3)
TCP provides reliable, in-order
byte-stream transfer (“pipe”)
between client and server processes
Application viewpoint

## Slide 113: Client/server socket interaction: TCP
server (running on hostid)
client
wait for incoming
connection request
connectionSocket =
serverSocket.accept()
create socket,
port=x, for incoming request:
serverSocket = socket()
create socket,
connect to hostid, port=x
clientSocket = socket()
send request using
clientSocket
read request from
connectionSocket
write reply to
connectionSocket
TCP
connection setup
close
connectionSocket
read reply from
clientSocket
close
clientSocket

## Slide 114: Example app: TCP client
from socket import *
serverName = 'servername'
serverPort = 12000
clientSocket = socket(AF_INET, SOCK_STREAM)
clientSocket.connect((serverName,serverPort))
sentence = input('Input lowercase sentence:')
clientSocket.send(sentence.encode())
modifiedSentence = clientSocket.recv(1024)
print ('From Server:', modifiedSentence.decode())
clientSocket.close()
Python TCPClient
create TCP socket for server, remote port 12000
No need to attach server name, port
Note: this code update (2023) to Python 3

## Slide 115: Example app: TCP server
from socket import *
serverPort = 12000
serverSocket = socket(AF_INET,SOCK_STREAM)
serverSocket.bind(('',serverPort))
serverSocket.listen(1)
print('The server is ready to receive')
while True:
connectionSocket, addr = serverSocket.accept()
sentence = connectionSocket.recv(1024).decode()
capitalizedSentence = sentence.upper()
connectionSocket.send(capitalizedSentence.
encode())
connectionSocket.close()
Python TCPServer
create TCP welcoming socket
server begins listening for incoming TCP requests
loop forever
server waits on accept() for incoming requests, new socket created on return
read bytes from socket (but not address as in UDP)
close connection to this client (but not welcoming socket)
Note: this code update (2023) to Python 3

## Slide 116: Chapter 2: Summary
application architectures
  client-server
  P2P
application service requirements:
  reliability, bandwidth, delay
Internet transport service model
  connection-oriented, reliable: TCP
  unreliable, datagrams: UDP
our study of network application layer is now complete!
specific protocols:
  HTTP
  SMTP, IMAP
  DNS
  P2P: BitTorrent
video streaming, CDNs
socket programming:
TCP, UDP sockets

## Slide 117: Chapter 2: Summary
Most importantly: learned about protocols!
Important themes:
typical client/server request/reply message exchange
centralized vs. decentralized
stateless vs. stateful
scalability
reliable vs. unreliable message transfer
“complexity at network edge”

## Slide 118: Additional Chapter 2 slides
JFK note: the timeout slides are important IMHO if one is doing a programming assignment (especially an RDT programming assignment in Chapter 3), since students will need to use timers in their code, and the TRY/EXCEPT is really the easiest way to do this. I introduce this here in Chapter 2 with the socket programming assignment since it teaches something (how to handle exceptions/timeouts), and lets students learn/practice that before doing the RDT programming assignment, which is harder
Notes: Version History
7.01 (January 2020)
All slides reformatted for 16:9 aspect ratio
Use of Calibri font, rather that Gill Sans MT
Updated slide content for 2020 link technologies and applications
Add more animation throughout
New Master slide

## Slide 119: Socket programming: waiting for multiple events
timeout
handle timeout
…
…
receive a message
sometimes a program must wait for one of several events to happen, e.g.,:
  wait for either (i) a reply from another end of the socket, or (ii) timeout: timer
  wait for replies from several different open sockets: select(), multithreading
timeouts are used extensively in networking
using timeouts with Python socket:
socket()
connect()
send()
recv()
throw exception
Show example: connect wordle client to random port, it will freeze.
settimeout()
handle exception
Notes: This is going to be something new for some students. Interruption-driven programming, timeout.

## Slide 120
s.settimeout(30)
s.recv()
timer starts!
interrupt s.recv() &
raise timeout exception
timeout
s.settimeout(10)
s.recv()
timer starts!
receive a message
& timer stop!
s.recv()
timer starts!
interrupt s.recv() &
raise timeout exception
timeout
Set a timeout on all future socket operations of that specific socket!
no packet arrives in 30 secs
no packet arrives in 10 secs
How Python socket.settimeout() works?

## Slide 121
Execute a block of code, and handle “exceptions” that may occur when executing that block of code
Python try-except block
try: <do something> except <exception>: <handle the exception>
Executing this try code block may cause exception(s) to catch. If an exception is raised, execution jumps from jumps directly into except code block
this except code block is only executed if an <exception> occurred in the try code block (note: except block is required with a try block)

## Slide 122: Socket programming: socket timeouts
from socket import *
serverPort = 12000
serverSocket = socket(AF_INET,SOCK_STREAM)
serverSocket.bind(('',serverPort))
serverSocket.listen(1)
counter = 0
while counter < 3:
connectionSocket, addr = serverSocket.accept()
connectionSocket.settimeout(10)
try:
wolf_location = connectionSocket.recv(1024).decode()
send_hunter(wolf_location) # a villager function
connectionSocket.send('hunter sent')
except timeout:
counter += 1
connectionSocket.close()
Python TCPServer (Villagers)
set a 10-seconds timeout on all future socket operations
catch socket timeout exception
timer starts when recv() is called and will raise timeout exception if there is no message within 10 seconds.
Use settimeout(None). settimeout(0) will result in changing the socket to non-blocking mode.
How to remove settimeout()?
- A shepherd boy tends his master’s sheep.
- If he sees a wolf, he can send a message to villagers for help using a TCP socket.
- The boy found it fun to connect to the server without sending any messages. But the villagers don’t think so.
- And they decided that if the boy connects to the server and doesn’t send the wolf location within 10 seconds for three times, they will stop listening to him forever and ever.
Toy Example:
Notes: Talk a bit about real-world examples for timeout at the end.
Question: settimeout(10), then what happens in the next iteration? Will .accept() have timeout?
Non-blocking:
https://www.scottklement.com/rpg/socktut/nonblocking.html

## Slide 123: Sample SMTP interaction
S: 220 hamburger.edu
C: HELO crepes.fr
S: 250 Hello crepes.fr, pleased to meet you
C: MAIL FROM: <alice@crepes.fr>
S: 250 alice@crepes.fr... Sender ok
C: RCPT TO: <bob@hamburger.edu>
S: 250 bob@hamburger.edu ... Recipient ok
C: DATA
S: 354 Enter mail, end with "." on a line by itself
C: Do you like ketchup?
C: How about pickles?
C: .
S: 250 Message accepted for delivery
C: QUIT
S: 221 hamburger.edu closing connection
Notes: Retired this slide, since telnet isn’t really used anymore, and few non https: mail servers around anymore....

## Slide 124: CDN content access: a closer look
netcinema.com
KingCDN.com
1
1. Bob gets URL for video http://netcinema.com/6Y7B23V
from netcinema.com web page
2
2. resolve http://netcinema.com/6Y7B23V
via Bob’s local DNS
netcinema’s
authoritative DNS
3
3. netcinema’s DNS returns CNAME for
http://KingCDN.com/NetC6y&B23V
4
5
6. request video from
KINGCDN server,
streamed via HTTP
KingCDN
authoritative DNS
Bob’s
local DNS
server
Bob (client) requests video http://netcinema.com/6Y7B23V
video stored in CDN at http://KingCDN.com/NetC6y&B23V
Notes: This slide retired, since there’s the Netflix example which is visually better

## Slide 125: Case study: Netflix
1
Bob manages Netflix account
Netflix registration,
accounting servers
Amazon cloud
CDN
server
2
Bob browses
Netflix video
Manifest file, requested
returned for
specific video
DASH server selected, contacted, streaming begins
upload copies of multiple versions of video to CDN servers
CDN
server
CDN
server
3
4
Notes: This slide retired, since there’s the new Netflix example which is visually better